## Slide 1: Lecture 11: Multithreading + VLIW
Tushar Krishna
School of Electrical and Computer Engineering
Georgia Institute of Technology
tushar@ece.gatech.edu
ECE4100/ECE6100/CS4290/CS6290
Advanced Computer Architecture
Fall 2016
http://tusharkrishna.ece.gatech.edu/teaching/aca_f16/
Acknowledgment: Lecture slides adapted from MIT EECS 6.823 (Arvind and J. Emer) and UCB CS 252 (K. Asanovic)

## Slide 2: Announcement
Midterm I
  In class
  Closed book and closed notes
  Any information regarding ISAs or formats will be provided

## Slide 3: Topics for Today
Multithreading
VLIW/EPIC

## Slide 4: Motivation: Pipeline Hazards
Each instruction may depend on the next
Even bypassing does not eliminate all delays
LW r1, 0(r2)
LW r5, 12(r1)
ADDI r5, r5, #12
SW 12(r1), r5
F
D
X
M
W
t0
t1
t2
t3
t4
t5
t6
t7
t8
F
D
X
M
W
D
D
D
F
D
X
M
W
D
D
D
D
D
D
F
D
D
D
D
t9
t10
t11
t12
t13
t14
D
D
D
D
D
D

## Slide 5: Motivation: Memory Delays
Superscalar and Out of Order Execution can help hide some of the stalls, but extracting enough ILP to hide all of the stalls is very hard.
F
D
X
M
W
t0
t1
t2
t3
t4
t5
t6
t7
t8
F
D
X
M
W
D
D
D
F
t9
t10
t11
t12
t13
t14
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
F
Cache Miss
LW r1, 0(r2)
LW r5, 12(r1)
ADDI r5, r5, #12
SW 12(r1), r5

## Slide 6: Multithreading
How can we guarantee no dependencies between instructions in a pipeline?
How can we perform useful work while pipeline is stalled due to memory?
One way is to interleave execution of instructions from different program threads on same pipeline

## Slide 7: Multithreading: Hiding Pipeline Dependencies
F
D
X
M
W
t0
t1
t2
t3
t4
t5
t6
t7
t8
T1: LW r1, 0(r2)
T2: ADD r7, r1, r4
T3: XORI r5, r4, #12
T4: SW 0(r7), r5
T1: LW r5, 12(r1)
t9
F
D
X
M
W
F
D
X
M
W
F
D
X
M
W
F
D
X
M
W
Interleave 4 threads, T1-T4, on non-bypassed 5-stage pipe
Prior instruction in a thread always completes write-back before next instruction in same thread reads register file
LW r1, 0(r2)
LW r5, 12(r1)
ADDI r5, r5, #12
SW 12(r1), r5
F
D
X
M
W
t0
t1
t2
t3
t4
t5
t6
t7
t8
F
D
X
M
W
D
D
D
F
D
X
M
W
D
D
D
D
D
D
F
D
D
D
D
t9
t10
t11
t12
t13
t14
D
D
D
D
D
D

## Slide 8: Multithreading: Hiding Memory Delay
F
D
X
M
W
t0
t1
t2
t3
t4
t5
t6
t7
t8
F
D
X
M
W
D
D
D
F
t9
t10
t11
t12
t13
t14
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
F
Cache Miss
LW r1, 0(r2)
LW r5, 12(r1)
ADDI r5, r5, #12
SW 12(r1), r5
F
D
X
M
W
t0
t1
t2
t3
t4
t5
t6
t7
t8
F
D
X
M
t9
t10
t11
t12
t13
t14
W
F
D
X
M
W
F
D
X
M
W
Cache Miss
F
D
D
D
D
D
D
T1: LW r1, 0(r2)
T2: ADD r7, r1, r4
T3: XORI r5, r4, #12
T4: SW 0(r7), r5
T1: LW r5, 12(r1)
D
Interleave 4 threads, T1-T4, on non-bypassed 5-stage pipe

## Slide 9: Implementing Multithreading
What does it mean to be a hardware thread?
  Each thread has its own PC
  Each thread has its own GPRs

## Slide 10: Simple Multithreaded Pipeline
Have to carry thread select down pipeline to ensure correct state bits read/written at each pipe stage
Each thread in hardware appears to OS as a CPU
+1
2
Thread select
PC
1
PC
1
PC
1
PC
1
I$
IR
GPR1
GPR1
GPR1
GPR1
X
Y
2
D$

## Slide 11: Implementing Multithreading
What does it mean to be a hardware thread?
  User State
    Each thread has its own PC
    Each thread has its own GPRs
  System State
    Each thread has its own Virtual Memory Page Table Base Register
    Each thread has its own Exception Handling Register

## Slide 12: Implementing Multithreading
In other words, multi-threading  replicate individual “context” but share pipeline control path and datapath (functional units and caches)
  In a multi-processor, the control path and datapath will also be replicated
Potential Performance Issues
  Increased conflicts in Caches
  Increased conflicts in TLBs
  Branch Predictor entry aliasing

## Slide 13: Types of Threads
A thread as a process (e.g., Posix)
  A thread has its own address space; these can be shared explicitly via programming
  At the processor level each thread will need its own PC, Register file and address translation (TLBs and page tables)
Lightweight threads
  Operate out of the same address space but still require private PC and RF
    Example kernel threads or shared memory user threads

## Slide 14: CDC 6600 Peripheral Processors (Cray, 1964)
First multithreaded hardware
10 “virtual” I/O processors
Fixed interleave on simple pipeline
Pipeline has 100ns cycle time
Each virtual processor executes one instruction every 1000ns
Accumulator-based instruction set to reduce processor state

## Slide 15: Thread Scheduling Policies
Fixed interleave (CDC 6600 PPUs, 1965)
  each of N threads executes one instruction every N cycles
  if thread not ready to go in its slot, insert pipeline bubble
Software-controlled interleave (TI ASC PPUs, 1971)
  OS allocates S pipeline slots amongst N threads
  if thread not ready to go in its slot, insert pipeline bubble
Hardware-controlled thread scheduling (HEP, 1982)
  hardware keeps track of which threads are ready to go
  picks next thread to execute based on scheduling scheme

## Slide 16: Hardware Thread Scheduling
Fine-grained multithreading
  Context switch among threads every cycle
Coarse-grained multithreading
  Context switch among threads every few cycles
  When?
    Function unit data hazard,
    L1 miss,
    L2 miss…
Choice depends on
  Context-switch overhead
  Number of threads supported (due to per-thread state)
  Expected application-level parallelism…

## Slide 17: Commercial Machines with Coarse Grain Multi-Threading
MIT Alewife (1990)
  4 threads per node
  Switch thread on local cache miss
IBM PowerPC RS64-IV (2000)
  2-Issue, 5-stage Pipeline
  2 threads per CPU
  On L2 miss, pipeline flushed and execution switches to second thread
Sun (now Oracle) Niagara
  multiple simple cores each with multiple hardware threads
    Niagara 1 (2004): 8 cores, 4 threads/core
    T4 (2012): 16 cores, 8 threads/core
  reduced energy/operation though much lower single thread performance
Notes: IBM PowerPC:
  - flush pipeline to simplify exception handling
  - short pipeline minimizes flush penalty (4 cycles), small compared to memory access latency

## Slide 18: How many threads?
Question
  Suppose every 4th instruction is a memory access
  Every memory access takes 512 cycles
    No caches in the CPU
    No out of order issue
  How many threads do you need to completely hide the memory delay?
    Little’s Law again!
    Need 512/4 = 128-threads to hide delay (+1 current thread) = 129 in total
    Performance
      Per Thread CPI: 4 + 512 = 516 cycles / 4 Instr = 129
      Overall CPI: 1
Tera (now Cray) MTA (1990)
  Up to 128 threads per processor
  No cache
    For supercomputing applications with large data sets and low locality
  Switch thread on every memory access

## Slide 19: Thread Selection
Time (processor cycle)
Superscalar
Fine
Grained
Coarse
Grained
Multi-
processing
Thread 2
Thread 4
Idle slot
Thread 1
Thread 3
Thread 5
Issue width
Simultaneous
Multithreading

## Slide 20: O-o-O Simultaneous Multithreading [Tullsen, Eggers, Emer, Levy, Stamm, Lo, DEC/UW, 1996]
Add multiple contexts and fetch engines
  allow instructions fetched from different threads to issue simultaneously
Utilize wide out-of-order superscalar processor issue queue to find instructions to issue from multiple threads
OOO instruction window already has most of the circuitry required to schedule from multiple threads
Any single thread can utilize whole machine

## Slide 21: Basic Out-of-Order Pipeline
Fetch
Decode/Map
Queue
Reg Read
Execute
Dcache/Store Buffer
Reg Write
Retire
PC
Icache
Register Map
Dcache
Regs
Regs
Threads can be mixed
[ EV8 – Microprocessor Forum, Oct 1999]
Notes: Here is a high level picture of the normal flow of pipeline...
The flow through this pipeline is…
If we assume that instructions can come from different threads, we observe that after renaming instructions are “thread-blind” since the instruction dependencies are fully reflected in the register dependencies, and the instructions from different threads could be mixed at will. This partitions the pipeline into two pieces - a thread-dependent part and a thread-independent part.

## Slide 22: SMT Pipeline
Fetch
Decode/Map
Queue
Reg Read
Execute
Dcache/Store Buffer
Reg Write
Retire
Icache
Dcache
PC
Register Map
Regs
Regs
[ EV8 – Microprocessor Forum, Oct 1999]
Notes: Now we enhance the pipeline by allowing fetch of instruction from multiple program counters.
Each cycle we pick a thread to fetch from.
The instructions are fetched out of a completed shared instruction cache,
and sent on to the mapper where separate maps are maintained for each thread.
Then the instructions are dropped into the queue and because the dependencies are all determined by the physical register dependencies, instructions from different threads can be mixed in all subsequence stages of the pipeline, as illustrated by the showing all the units uniformly shared by all the threads.

## Slide 23: SMT adapts to parallelism type
For regions with high thread-level parallelism (TLP) entire machine width is shared by all threads
Issue width
Time
Issue width
Time
For regions with low thread-level parallelism (TLP) entire machine width is available for instruction-level parallelism (ILP)

## Slide 24: Pentium-4 Hyperthreading (2002)
First commercial SMT design (2-way SMT)
  Hyperthreading == SMT
Logical processors share nearly all resources of the physical processor
  Caches, execution units, branch predictors
Die area overhead of hyperthreading ~ 5%
When one logical processor is stalled, the other can make progress
  No logical processor can use all entries in queues when two threads are active
Processor running only one active software thread runs at approximately same speed with or without hyperthreading
Notes: Separate Return Address Stack Per thread
Separate First-Level Global Branch History Table
Shared 2nd level BHT tagged with logical processor IDs

## Slide 25: Pentium-4 Hyperthreading Execution Pipeline

## Slide 26: Topics for Today
Multithreading
VLIW/EPIC

## Slide 27: ILP needed to keep pipelines full
Issue width
Time

## Slide 28: Example: Pipelined ILP Machine
One Pipeline Stage
Two Integer Units,
Single Cycle Latency
Two Load/Store Units,
Three Cycle Latency
Two Floating-Point Units,
Four Cycle Latency
Max Throughput, Six Instructions per Cycle
Latency in Cycles
How much instruction-level parallelism (ILP) is required to keep machine pipelines busy?
2x1 + 2x3 + 2x4 = 16

## Slide 29: Superscalar Control Logic Scaling
Each issued instructions must make interlock checks against W*L instructions, i.e., growth in interlocks  W*(W*L)
For in-order machines, L is related to pipeline latencies
For out-of-order machines, L also includes time spent in ROB
As W increases, larger instruction window is needed to find enough parallelism to keep machine busy  greater L
Lifetime L
Issue Group
Previously Issued Instructions
Issue Width W

## Slide 30: Sequential ISA Bottleneck
Check instruction dependencies
Superscalar processor
a = foo(b);
for (i=0, i<
Sequential source code
Parallel compiler
Find independent operations
Schedule operations
Sequential machine code

## Slide 31: VLIW: Very Long Instruction Word
Multiple operations packed into one instruction
Each operation slot is for a fixed function
Constant operation latencies are specified
Two Integer Units,
Single Cycle Latency
Two Load/Store Units,
Three Cycle Latency
Two Floating-Point Units,
Four Cycle Latency
Int Op 2
Mem Op 1
Mem Op 2
FP Op 1
FP Op 2
Int Op 1

## Slide 32: VLIW Design Principles
The architecture:
  Parallelism within an instruction
    No RAW check
  Provides deterministic latency for all operations
  No data use allowed before data ready
    no data interlocks
The compiler:
  Schedules (reorders) to maximize parallel execution
  Guarantees intra-instruction parallelism
  Schedules to avoid data hazards (no interlocks)
    Typically separates operations with explicit NOPs

## Slide 33: Early VLIW Machines
FPS AP120B (1976)
  scientific attached array processor
  first commercial wide instruction machine
  hand-coded vector math libraries using software pipelining and loop unrolling
Multiflow Trace (1987)
  commercialization of ideas from Fisher’s Yale group including “trace scheduling”
  available in configurations with 7, 14, or 28 operations/instruction
  28 operations packed into a 1024-bit instruction word
Cydrome Cydra-5 (1987)
  7 operations encoded in 256-bit instruction word
  rotating register file

## Slide 34: Loop Execution
How many FP ops/cycle?
for (i=0; i<N; i++)
B[i] = A[i] + C;
Int1
Int 2
M1
M2
FP+
FPx
loop:
ld
add r1
fadd
sd
add r2
bne
1 fadd / 8 cycles = 0.125
loop: ld f1, 0(r1)
add r1, 8
fadd f2, f0, f1
sd f2, 0(r2)
add r2, 8
bne r1, r3, loop
Compile
Schedule
Notes: Software Pipeling: if iterations from loops are independent, then can get ILP by taking instructions from different iterations

## Slide 35: Loop Unrolling
for (i=0; i<N; i++)
B[i] = A[i] + C;
for (i=0; i<N; i+=4)
{
B[i] = A[i] + C;
B[i+1] = A[i+1] + C;
B[i+2] = A[i+2] + C;
B[i+3] = A[i+3] + C;
}
Unroll inner loop to perform 4 iterations at once
Is this code correct?
No, need to handle values of N that are not multiples of unrolling factor with final cleanup loop

## Slide 36: Scheduling Loop Unrolled Code
loop: ld f1, 0(r1)
ld f2, 8(r1)
ld f3, 16(r1)
ld f4, 24(r1)
add r1, 32
fadd f5, f0, f1
fadd f6, f0, f2
fadd f7, f0, f3
fadd f8, f0, f4
sd f5, 0(r2)
sd f6, 8(r2)
sd f7, 16(r2)
sd f8, 24(r2)
add r2, 32
bne r1, r3, loop
Schedule
Int1
Int 2
M1
M2
FP+
FPx
loop:
Unroll 4 ways
ld f1
ld f2
ld f3
ld f4
add r1
fadd f5
fadd f6
fadd f7
fadd f8
sd f5
sd f6
sd f7
sd f8
add r2
bne
How many FLOPS/cycle?
4 fadds / 11 cycles = 0.36

## Slide 37: Software Pipelining
How many FLOPS/cycle?
loop: ld f1, 0(r1)
ld f2, 8(r1)
ld f3, 16(r1)
ld f4, 24(r1)
add r1, 32
fadd f5, f0, f1
fadd f6, f0, f2
fadd f7, f0, f3
fadd f8, f0, f4
sd f5, 0(r2)
sd f6, 8(r2)
sd f7, 16(r2)
add r2, 32
sd f8, -8(r2)
bne r1, r3, loop
Int1
Int 2
M1
M2
FP+
FPx
Unroll 4 ways first
ld f1
ld f2
ld f3
ld f4
fadd f5
fadd f6
fadd f7
fadd f8
sd f5
sd f6
sd f7
sd f8
add r1
add r2
bne
ld f1
ld f2
ld f3
ld f4
fadd f5
fadd f6
fadd f7
fadd f8
sd f5
sd f6
sd f7
sd f8
add r1
add r2
bne
ld f1
ld f2
ld f3
ld f4
fadd f5
fadd f6
fadd f7
fadd f8
sd f5
add r1
loop:
iterate
prolog
epilog
4 fadds / 4 cycles = 1

## Slide 38: Software Pipelining vs. Loop Unrolling
time
performance
time
performance
Loop Unrolled
Software Pipelined
Startup overhead
Wind-down overhead
Loop Iteration
Loop Iteration
Software pipelining pays startup/wind-down costs only once per loop, not once per iteration

## Slide 39: What if there are no loops?
Branches limit basic block size in control-flow intensive irregular code
Difficult to find ILP in individual basic blocks
Basic block

## Slide 40: Trace Scheduling [Fisher, Ellis]
Pick string of basic blocks, a trace, that represents most frequent branch path
Schedule whole “trace” at once
Add fixup code to cope with branches jumping out of trace
How do we know which trace to pick?
Use profiling feedback or compiler heuristics to find common branch paths

## Slide 41: Problems with “Classic” VLIW
Knowing branch probabilities
  Profiling requires an significant extra step in build process
Object code size
  instruction padding wastes instruction memory/cache
  loop unrolling/software pipelining replicates code
Scheduling variable latency memory operations
  caches and/or memory bank conflicts impose statically unpredictable variability
Scheduling for statically unpredictable branches
  optimal schedule varies with branch path
Object-code compatibility
  have to recompile all code for every machine, even for two machines in same generation

## Slide 42: Cydra-5: Memory Latency Register (MLR)
Problem: Loads have variable latency
Solution: Let software choose desired memory latency
  Compiler schedules code for maximum load-use distance
  Software sets MLR to latency that matches code schedule
  Hardware ensures that loads take exactly MLR cycles to return values into processor pipeline
    Hardware buffers loads that return early
    Hardware stalls processor if loads return late

## Slide 43: Intel EPIC IA-64
Explicitly Parallel Instruction Computing
  EPIC is the style of architecture (cf. CISC, RISC)
IA-64 was Intel’s chosen ISA (cf. x86, MIPS)
  IA-64 = Intel Architecture 64-bit
  An object-code compatible VLIW
Itanium (aka Merced) was first implementation (c.f. 8086)
  First customer shipment expected 1997 (actually 2001)
  McKinley, second implementation shipped in 2002

## Slide 44: IA-64 Instruction Format and Registers
128 General Purpose 64-bit Integer Registers
128 General Purpose 64/80-bit Floating Point Registers
64 1-bit Predicate Registers
GPRs rotate to reduce code size for software pipelined loops
Instruction 2
Instruction 1
Instruction 0
Template
128-bit instruction bundle

## Slide 45: IA-64 Predicated Execution
Problem: Mispredicted branches limit ILP
Solution: Eliminate hard to predict branches with predicated execution
Inst 1
Inst 2
br a==b, b2
Inst 3
Inst 4
br b3
Inst 5
Inst 6
Inst 7
Inst 8
b0:
b1:
b2:
b3:
if
else
then
Four basic blocks
Inst 1
Inst 2
p1,p2 <- cmp(a==b)
(p1) Inst 3 || (p2) Inst 5
(p1) Inst 4 || (p2) Inst 6
Inst 7
Inst 8
Predication
One basic block
Mahlke et al, ISCA95: On average >50% branches removed
  Instruction becomes NOP if predicate register false
  Almost all IA-64 instructions can be executed conditionally under predicate
Notes: When does predicated instruction become NOP?
At commit.

## Slide 46: IA-64 Speculative Execution
Problem: Branches restrict compiler code motion
Inst 1
Inst 2
br a==b, b2
Load r1
Use r1
Inst 3
Can’t move load above branch because might cause spurious exception
Load.s r1
Inst 1
Inst 2
br a==b, b2
Chk.s r1
Use r1
Inst 3
Speculative load but sets “poison” bit on destination register if exception
Check for exception in original home block jumps to fixup code if exception detected
Particularly useful for scheduling long latency loads early
Solution: Speculative operations that don’t cause exceptions

## Slide 47: Eight Core Itanium “Poulson” [2012]
544mm2 in 32nm CMOS
Over 3 billion transistors
8 cores
  2-way multi-threaded
  6 instruction/cycle fetch
    Two 128-bit bundles
  Up to 12 insts/cycle execute
1-cycle 16KB L1 I&D caches
9-cycle 512KB L2 I-cache
8-cycle 256KB L2 D-cache
32 MB shared L3 cache
Last Itanium to be released so far.
Rumors of one more “Kittson” to be released mid-2017.

## Slide 48: Itanium Sales
Source: Wikipedia
“Itanic”
Notes: Itanic (The unsinkable chip) coined by ”The Register” in Oct 1999, right after Intel announced the name “Itanium”..

## Slide 49: VLIW Summary
Motivation: reduce hardware complexity by putting static analysis (compiler) to work
Limits of Static Scheduling
  Unpredictable branches
  Variable memory latency (unpredictable cache misses)
  Code size explosion
  Compiler complexity
  Machine code is specific to a model
Despite several attempts, VLIW has failed in general-purpose computing arena (so far).
  More complex VLIW architectures close to in-order superscalar in complexity, no real advantage on large complex apps.
Successful in embedded DSP market
  Simpler VLIWs with more constrained environment, friendlier code.