## Slide 1: Lecture 12: Cache Basics
Tushar Krishna
School of Electrical and Computer Engineering
Georgia Institute of Technology
tushar@ece.gatech.edu
ECE4100/ECE6100/CS4290/CS6290
Advanced Computer Architecture
Fall 2016
http://tusharkrishna.ece.gatech.edu/teaching/aca_f16/
Acknowledgment: Lecture slides adapted from UCB CS252 (K. Asanovic),
MIT EECS 6.823 (Arvind and J. Emer) and GT CS 4290/6290 (M. Pruvolic)

## Slide 2: Memory in a Modern System
CORE 1
L2 CACHE 0
SHARED L3 CACHE
DRAM INTERFACE
CORE 0
CORE 2
CORE 3
L2 CACHE 1
L2 CACHE 2
L2 CACHE 3
DRAM BANKS
DRAM MEMORY CONTROLLER
Memory
CPU
50-80% of area dedicated to memory!

## Slide 3: CPU-Memory Bottleneck
Memory
CPU
Performance of high-speed computers is usually limited by memory latency & bandwidth
  Latency (time for a single access)
    Memory access time >> Processor cycle time
  Bandwidth (number of accesses per unit time)
    if fraction m of instructions access memory,
    => 1+m memory references / instruction
    => For CPI = 1, need 1+m memory refs / cycle

## Slide 4: Early Read-Only Memory Technologies
Punched cards, From early 1700s through Jaquard Loom, Babbage, and then IBM
Punched paper tape, instruction stream in Harvard Mark 1
IBM Card Capacitor ROS
IBM Balanced Capacitor ROS
Diode Matrix, EDSAC-2 µcode store

## Slide 5: Early Read/Write Memory Technologies
Williams Tube, Manchester Mark 1, 1947
Babbage, 1800s: Digits stored on mechanical wheels
Mercury Delay Line, Univac 1, 1951
Also, regenerative capacitor memory on Atanasoff-Berry computer, and rotating magnetic drum memory on IBM 650

## Slide 6: Core Memory
Core memory was first large scale reliable main memory
  invented by Forrester in late 40s/early 50s at MIT for Whirlwind project
  Robust, non-volatile storage
Bits stored as magnetization polarity on small ferrite cores threaded onto two-dimensional grid of wires
  Cores threaded onto wires by hand (25 billion a year at peak production)
  Core access time ~ 1µs
Coincident current pulses on X and Y wires would write cell and also sense original state (destructive reads)
Used on space shuttle computers
DEC PDP-8/E Board,
4K words x 12 bits, (1968)
MIT Whirlwind Core Memory
Notes: What is non-volatile?

## Slide 7: Semiconductor Memory
Semiconductor memory began to be competitive in early 1970s
  Intel was formed to exploit market for semiconductor memory
  Early semiconductor memory was Static RAM (SRAM). SRAM cell internals similar to a latch (cross-coupled inverters).
First commercial Dynamic RAM (DRAM) was Intel 1103
  1Kbit of storage on single chip
  charge on a capacitor used to hold value
Semiconductor memory quickly replaced core in ‘70s

## Slide 8: “Memory” Today  DRAM
Dynamic random access memory
Capacitor charge state indicates stored value
  Whether the capacitor is charged or discharged indicates storage of 1 or 0
  1 capacitor
  1 access transistor
Capacitor leaks through the RC path
  DRAM cell loses charge over time
  DRAM cell needs to be refreshed
Select (word line)
Data (bitline)

## Slide 9: DRAM Organization
Bits stored in 2-dimensional arrays on chip
Modern chips have around 4 logical banks on each chip
  each logical bank physically implemented as many smaller arrays
Row Address Decoder
Col.
1
Col. 2M
Row 1
Row 2N
Column Decoder & Sense Amplifiers
M
N
N+M
bit lines
word lines
DRAM cell (one bit)
D
Data
More on DRAM in a later lecture!

## Slide 10: Processor-DRAM Gap (latency)
DRAM:
7%/year
MicroProccessors:
60%/year
“Moore’s Law”
Processor-Memory
Performance Gap: (grows 50% / year)
Four-issue 2GHz superscalar accessing 100ns DRAM could execute 800 instructions during time for one memory access!
What happened?
Later!

## Slide 11: Little’s Law
Throughput (T) = Number in Flight (N) / Latency (L)
Memory
CPU
Table of accesses in flight
Example:
      --- Assume infinite bandwidth memory
      --- 100 cycles / memory reference
      --- 1 + 0.2 memory references / instruction
      Table size = 1.2 * 100 = 120 entries
120 independent memory operations in flight!
Is it even possible for CPU to generate 120 independent memory requests?
Notes: We saw multi-threading as one solution for this.

## Slide 12: Mitigate Latency using Caches
Reduce average memory access latency (and energy) by using caches – small and fast memories that retain recently-accessed data
  Why would this help?
    Locality: Patterns of memory references made by a processor are often highly predictable
PC
96 …
100 loop: ADD r2, r1, r1
104 SUBI r3, r3, #1
BNEZ r3, loop
112 …

## Slide 13: Why would Caches help?
Two predictable properties of memory references:
  Temporal Locality: If a location is referenced it is likely to be referenced again in the near future.
  Spatial Locality: If a location is referenced it is likely that locations near it will be referenced in the near future.
Memory addresses A, B, C, A, B, C, A, B, C
Memory addresses A, A+1, A+2, A+3, A+4
Temporal
Spatial

## Slide 14: Exploiting Locality
Temporal locality
  Store recently accessed data in cache
    Anticipation: the data will be accessed again soon
Spatial locality
  Store addresses adjacent to the recently accessed one in automatically managed fast memory
    Logically divide memory into equal size blocks (called cache block or cache line)
    On accessing any word in the block, fetch the entire line
    Anticipation: nearby data will be accessed soon

## Slide 15: Caches  SRAM
Static random access memory
Two cross coupled inverters store a single bit
  Feedback path enables the stored value to persist in the “cell”
  4 transistors for storage
  2 transistors for access
Word line
bitline
_bitline

## Slide 16: Memory Hierarchy
size: Register << SRAM << DRAM why?
latency: Register << SRAM << DRAM why?
bandwidth: on-chip >> off-chip why?
On a data access:
  hit (data Î fast memory)  low latency access
  miss (data Ï fast memory)  high latency access (DRAM)
Small,
Fast Memory
(RF, SRAM)
CPU
Big, Slow Memory
(DRAM)
A
B
holds frequently used data
On-chip
Off-chip
Cost
Size
Cost + wire-delays
Notes: Due to cost
Due to size of DRAM
Due to cost and wire delays (wires on-chip cost much less, and are faster)

## Slide 17: Memory Hierarchy
100s Bytes
<10 ns
$$$
K Bytes
10-100 ns
1-0.1 cents/bit
M Bytes
200ns- 500ns
$.0001-.00001 cents /bit
G Bytes, 10 ms (10,000,000 ns)
10 - 10 cents/bit
-5
-6
Capacity
Access Time
Cost
infinite
sec-min
10 cents/bit
Registers
Cache
Memory
Disk
Tape
Instr. Operands
Cache Lines
Pages
Files
Staging
Transfer Unit
Compiler
1-8 bytes
Cache controller
8-128 bytes
Operating system
512-4K bytes
User
Mbytes
CAPACITY
SPEED and COST
-8
Notes: Memory: DRAM
Cache: SRAM

## Slide 18: Cache Basics
When data referenced
  HIT: If in cache, use cached data instead of accessing memory
    Hit ratio: hits/accesses
  MISS: If not in cache, bring block into cache from memory
    Maybe have to kick something else out to do it
    Time taken: miss penalty
    Miss ratio: misses/accesses = 1 – hit ratio

## Slide 19: Cache Design Decisions
Placement: where in the cache can a block go?
Identification: how do we find a block in cache?
Replacement: what to kick out to make room in cache?
Write policy: What do we do about stores?

## Slide 20: Cache Design Decisions
Placement: where in the cache can a block go?
Identification: how do we find a block in cache?
Replacement: what to kick out to make room in cache?
Write policy: What do we do about stores?

## Slide 21: Cache Placement
Word Number
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
Line Number
?
Set #
0
1
2
3
4
5
6
7
Direct
Mapped
one location
0
1
2
3
Way #
0
1
0
1
0
1
0
1
(2-way) Set
Associative
2 locations
0
1
2
3
4
5
6
7
Fully
Associative
anywhere
Searching easy but inefficient use of space
Searching more expensive
Cache
DRAM

## Slide 22: Cache Design Decisions
Placement: where in the cache can a block go?
Identification: how do we find a block in cache?
Replacement: what to kick out to make room in cache?
Write policy: What do we do about stores?

## Slide 23: Basic Principle: Address Breakdown
Same address can be interpreted in more than one way
0x80080000
0x80080004
4 byte (32-bit) word
16 byte line
4KB page
12
20
Page #/Page address
Byte within a page
0x80081000
Memory
0x80080008
0x8008000C
0x80080010
2
2
28
Byte in a line
Word in a line
Line #/address
Used by Cache
index
tag
offset
Depends on size of cache line, i.e., no of bytes in a cache line
Depends on number of lines in the cache
Remaining bits

## Slide 24: Microarchitecture: Direct Mapped Cache
Offset
Tag
Index
Block number
Block offset
Address:
index | v | tag | Data block |  |  | 
2k
lines
k-bits
b-bits
t-bits
Tag Array
Data Array

## Slide 25: Microarchitecture: Direct Mapped Cache
index | v | tag | Data block |  |  | 
Offset
Tag
Index
Block number
Block offset
Address:
k
2k
lines
=
t
HIT
b
Data Word or Byte
t

## Slide 26: Microarchitecture: Direct Mapped Cache
Offset
Tag
Index
Block number
Block offset
Address:
index | v | tag | Data block |  |  | 
2k
lines
k-bits
b-bits
t-bits
What is a bad reference pattern?
Strided at size of cache
Cache Data Array Size?
2k x 2b
Cache Tag Array Size?
2k x (1+t)
Tag Array
Data Array
Usually just called Cache Size
Notes: Corresponding misses are called “conflict misses”

## Slide 27: Direct Mapped Cache: higher-order vs. lower-order address bits
index | v | tag | Data block |  |  | 
Offset
Index
Tag
Block number
Block offset
Address:
k
2k
lines
=
t
HIT
b
Data Word or Byte
t
Why might this be undesirable?
Spatially local blocks conflict

## Slide 28: Hash Address Selection
index | v | tag | Data block |  |  | 
Offset
Address
k
2k
lines
=
t
HIT
b
Data Word or Byte
t
Hash
What are the tradeoffs of hashing?
Good: Regular strides don’t conflict
Bad: Hash adds latency Tag is larger

## Slide 29: Microarchitecture : Set-Associative Cache
Offset
Tag
Index
Address:
index | v | tag | Data block |  |  | 
2k
lines
k-bits
b-bits
t-bits
v | tag | Data block |  |  | 
Way 0
Way (a-1)
k
=
t
t
=
t
Data
Word
or Byte
b
…
…
a = associativity

## Slide 30: Microarchitecture : Set-Associative Cache
index | v | tag | Data block |  |  | 
k-bits
b-bits
t-bits
v | tag | Data block |  |  | 
Way (a-1)
Offset
Tag
Index
Address:
Cache Data Array Size?
2k x 2b x a
Cache Tag Array Size?
2k x (1+t) x a
a = associativity
…
Way 0

## Slide 31: Microarchitecture: Fully Associative Cache
Tag
Data Block
V
=
Block
Offset
Tag
t
b
HIT
Data
Word
or Byte
=
=
t
Cache Data Array Size?
2b x a
Cache Tag Array Size?
(1+t) x a

## Slide 32: Cache Design Decisions
Placement: where in the cache can a block go?
Identification: how do we find a block in cache?
Replacement: what to kick out to make room in cache?
Write policy: What do we do about stores?

## Slide 33: Cache Replacement
Direct Mapped?
  Kick out the line in the set
Set-Associative / Fully-Associative?
  Kick out one of the lines in the set
  Which one?
    Any empty one
    What if no line empty?
    “Replacement Policy”
      Random
      Least-Recently Used (LRU)
      Most-Recently Used (MRU)
      FIFO
Most Popular

## Slide 34: LRU Policy Example
A
B
C
D
MRU
LRU
LRU+1
MRU-1
Access C
C
A
B
D
Access D
D
C
A
B
Access E
E
D
C
A
Access C
C
E
D
A
Access G
G
C
E
D
MISS, replacement
needed
MISS, replacement
needed
    What happens to the line that is kicked out?
      Discard it as it is just a copy from memory, unless it is “dirty” (later in the lecture)

## Slide 35: Implementing LRU
True LRU
  Need to remember order in which all N lines were last accessed
    N! scenarios
      2 ways  AB BA = 2 = 2!
      3 ways  ABC ACB BAC BCA CAB CBA = 6 = 3!
    Need O(log N!) bits  O(N log N) LRU bits
  True LRU only feasible for small associativity

## Slide 36: Pseudo LRU
Way A
Way B
Way C
Way D
B1 == 0
B2 == 0
B0 == 0
Are all 4 lines valid?
Use an invalid line
N
Y
Y
Y
Y
N
N
N
State | Replace
00x | Way A
01x | Way B
1x0 | Way C
1x1 | Way D
Ref | Next state
A | 11_
B | 10_
C | 0_1
D | 0_0
x: don’t care
_: unchanged
Notes: Example Access Pattern:
B 10x
A 11x
C 011
D 010
Replace B =>
B 100
Replace C [should have been A in true LRU]

## Slide 37: Cache Design Decisions
Placement: where in the cache can a block go?
Identification: how do we find a block in cache?
Replacement: what to kick out to make room in cache?
Write policy: What do we do about stores?

## Slide 38: Write Policies
Write Hit Policy
  If a write hits in the cache, should the updated value stay in cache or go to memory?
Write Miss Policy
  If a write misses in the cache, should the line be brought into cache?

## Slide 39: Write Hit Policy: When to Write?
Write-through Cache
  The value is written to both the cache line and to the next level of memory concurrently
    + Keeps next-level cache / memory updated
    - has high memory traffic
Write-back Cache
  The value is written only to the cache line. The modified cache line is written to next level / main memory only when it has to be replaced.
    + Less memory traffic
    Typically preferred if lot of writes before a read!
    - Contents of next-level cache / memory can be stale
Notes: Suppose access stream:
LD 0x160 (A=3)
ST 0x160, 5
ST 0x160, 7
ST 0x160, 8
LD 0x160
Which is better?
Writeback.
Suppose 2 processors
P1: LD 0x160 (A=3)
ST A 0x160
P2: LD 0x160
Which is better?
Write-through

## Slide 40: Writeback Cache Microarchitecture
Each cache line has an additional dirty bit
Policy for dirty bit?
  When line first brought into cache, valid = 1, dirty = 0 (i.e., line is clean)
  On first write to (any word) on the line, dirty = 1
    Memory not updated yet, cache has the only up-to-date copy of data for a dirty line
  On replacement, dirty line written to memory
index | v | dirty | tag | Data block |  |  | 

## Slide 41: Write Miss Policy: Allocate or not?
Write-Allocate
  The line is allocated on a write miss, followed by the write hit actions
  Write misses first act like read misses
  Mostly used with write-back caches
Write No-Allocate
  Line is only updated in the lower level memory and not brought into the cache
  Mostly used with write-through caches
Notes: Question: Why does write miss need to bring line into cache? It will be over-written anyway.
Ans) A word in the line will be over-written. Still need rest of the line.
If a line is written but not likely to be read, better to do write no-allocate.
Otherwise it may kick out a useful line.