## Slide 1: Lecture 13: Cache Optimizations
Tushar Krishna
School of Electrical and Computer Engineering
Georgia Institute of Technology
tushar@ece.gatech.edu
ECE4100/ECE6100/CS4290/CS6290
Advanced Computer Architecture
Fall 2016
http://tusharkrishna.ece.gatech.edu/teaching/aca_f16/
Acknowledgment: Lecture slides adapted from MIT EECS 6.823 (Arvind and J. Emer) and GT ECE 4100/6100 (T. Conte)

## Slide 2: Cache Performance
Hit: data is in the cache
  Hit Time: Time to get data from the cache to the processor
Miss: date is not in the cache
  Miss Rate: Number of Misses / Total Accesses
  Miss Penalty: Time to get a missing block from lower levels of memory and get the data to the processor

## Slide 3: Types of Cache Misses
Compulsory
  first-reference to a block a.k.a. cold start misses
    misses that would occur even with infinite cache
Capacity
  cache is too small to hold all data the program needs
    misses that would occur even under perfect placement & replacement policy
Conflict
  misses from collisions due to block-placement strategy
    misses that would not occur with full associativity

## Slide 4: Effect of Cache Parameters on Performance
 | Larger capacity cache | Higher associativity cache | Larger Block Size*
Compulsory misses |  |  | 
Capacity misses |  |  | 
Conflict misses |  |  | 
Hit time |  |  | 
Miss penalty |  |  | 
*assume substantial spatial locality
Notes: Larger block size:
Miss Penalty might go up since more data has to be brought into cache as lower levels now take longer to access and require higher bandwidth

## Slide 5: AMAT
How to reduce AMAT?
  reduce the hit time
  reduce the miss rate
  reduce the miss penalty
Average Memory Access Time (AMAT) =
Hit time + Miss rate x Miss penalty
We will discuss a few cache optimizations in class for attacking each of these terms. More optimizations from Hennessy & Patterson Book are in T-square in Supplementary Material.
Notes: Example:
Hit Time = 1 cycle
Miss Rate = 8%
Miss Penalty = 100 cycles
AMAT = 1 + 0.08*100 = 9 cycles

## Slide 6: Reducing Miss Rate
Cache Parameters
  Size
  Associativity
  Block Size
Prefetch
Victim Cache

## Slide 7: Cache Parameters
 | Advantages | Disadvantages | Limit
Larger Cache Size | Fewer Capacity Misses | Larger Hit Latency Larger Area | 
Higher Associativity | Fewer Conflict Misses | Slower search time | 
Larger Block Size | More spatial locality | Higher Miss Penalty Cache Pollution | 
Miss rate
“diminishing returns”
log(cache size)
Miss rate
“diminishing returns”
log(associativity)
Miss rate
“cache pollution”
Block size
Compulsory Misses
Capacity Misses
Cache Pollution

## Slide 8: Reducing Miss Rate
Cache Parameters
  Size
  Associativity
  Block Size
Prefetch
Victim Cache

## Slide 9: Prefetching
Idea: get it before you need it
  Easier for instructions
  Harder for data
How does prefetching affect cache misses?
  Compulsory
  Capacity
  Conflict
Reduce
Increase
Increase

## Slide 10: Hardware Prefetching
+1 prefetch: fetch missing block, and next sequential block
  Works great for streams with high sequential locality -- e.g., instruction caches
  Uses unused memory bandwidth between misses
    Can affect miss penalty if bus to memory is busy and there’s a demand miss by the CPU
Strided prefetch
  Suppose the following code is being executed
      for (i = 1; i < MAX; i += n)
        a[i] = b[i];
  Prefetch block(s) +k, +2k, +3k, … +d*k

## Slide 11: Challenges with Prefetching
Prefetch on Miss or Access?
Usefulness – should produce hits
Timeliness – not late and not too early
Cache and bandwidth pollution

## Slide 12: Reducing Miss Rate
Cache Parameters
  Size
  Associativity
  Block Size
Prefetch
Victim Cache

## Slide 13: Victim Caches
Victim cache is a small associative back up cache, added to a direct mapped cache, which holds recently evicted lines
  Fast hit time of direct mapped but with reduced conflict misses!
L1 Data Cache
L2 or Mem
RF
CPU
Evicted data from L1
Evicted data from VC discarded since already send to Mem
Hit data (miss in L1)
Victim Cache
FA, 4 blocks
  First look up in direct mapped cache
  If miss, look in victim cache
  If hit in victim cache?
  If miss in victim cache?
swap hit line with line now evicted from L1
  L1 victim  VC, VC victim?

## Slide 14: Reducing Miss Penalty
Multi-level Caches
Early Restart/Critical Word First
Sectored Cache

## Slide 15: Reducing Miss Penalty
Multi-level Caches
Early Restart/Critical Word First
Sectored Cache

## Slide 16: Multilevel Caches
A memory cannot be large and fast
Add level of cache to reduce miss penalty
  Each level can have longer latency than level above
  So, increase sizes of cache at each level
CPU
L1
L2
DRAM
Metrics:
Local miss rate = misses in cache/ accesses to cache
Global miss rate = misses in cache / CPU memory accesses
Misses per instruction = misses in cache / number of instructions

## Slide 17: A typical memory hierarchy
L1 Data Cache
L1 Instruction Cache
Unified L2 Cache
RF
Memory
Memory
Memory
Memory
Multiported register file (part of CPU)
Split instruction & data primary caches
(on-chip SRAM)
Multiple interleaved memory banks (DRAM)
Large unified secondary cache (on-chip SRAM)
CPU

## Slide 18: Intel Haswell (2013)
64B Cache Lines
L1 Instruction Cache: 32 KB, 8-way, 4-cycle latency
L1 Data Cache: 32 KB, 8-way, 4-5 cycle latency
L2 Cache: 256 KB, 8-way, 12 cycles
L3 Cache: 8 MB, 12-way, 36 cycles
(Last Level Cache or LLC)
22nm
1.4B Transistors
Die Size: 177mm2

## Slide 19: Example: AMAT with L2
L1 cache
L2 cache
main memory
5 cycles
50 cycles
AMAT = Hit TimeL1 + Miss RateL1 x Miss PenaltyL1
Miss PenaltyL1 = Hit TimeL2 + Miss RateL2 x Miss PenaltyL2
Suppose
Miss RateL1 = 10%
Miss RateL2 = 6%
Miss PenaltyL1 = 5 + 0.06x50 = 8 cycles
AMATL1 = 2 + 0.1x8 = 2.8 cycles
2 cycles
ignore interconnect delays
If no L2:
AMATL1 = 2 + 0.1x50 = 7 cycles

## Slide 20: Inclusion Policy
Inclusive multi-level cache:
  Inner cache holds copies of data in outer cache
Exclusive multi-level caches:
  Inner cache data is not in outer cache
    Swap lines between inner/outer caches on miss
Non-inclusive multi-level cache
  Inner cache may hold data not in the outer cache

## Slide 21: Miss, Replacement and Invalidation with L1 and L2
Inclusion Policy | L1 Miss |  | L1 Replace-ment | L2 Invalidation
 | L2 Miss | L2 Hit |  | 
Inclusive L2 |  |  |  | 
Non-Inclusive L2 |  |  |  | 
Exclusive L2 |  |  |  | 
Allocate L1 and L2
Allocate both L1 and L2
Allocate only L1
L2 untouched*
If not in L2, add to L2
Allocate
in L2
*except Writeback
Check L1 only if present in L2
Always check L1
Check L1 only if not present in L2
L2 replacement?
Kick out line from L1 in case of Inclusive
Allocate L1
Swap line with L1
Allocate L1
Notes: L1 replacement needs to writeback to L2 in Inclusive L2 design.