## Slide 1: Lecture 14: Cache Optimizations + Demand Paging
Tushar Krishna
School of Electrical and Computer Engineering
Georgia Institute of Technology
tushar@ece.gatech.edu
ECE4100/ECE6100/CS4290/CS6290
Advanced Computer Architecture
Fall 2016
http://tusharkrishna.ece.gatech.edu/teaching/aca_f16/
Acknowledgment: Lecture slides adapted from MIT EECS 6.823 (Arvind and J. Emer) GT ECE 4100/6100 (T. Conte), UCB CS 252 (K. Asanovic) and UW CS 378 (L. Ceze)

## Slide 2: AMAT
How to reduce AMAT?
  reduce the hit time
  reduce the miss rate
  reduce the miss penalty
Average Memory Access Time (AMAT) =
Hit time + Miss rate x Miss penalty
Notes: Example:
Hit Time = 1 cycle
Miss Rate = 8%
Miss Penalty = 100 cycles
AMAT = 1 + 0.08*100 = 9 cycles

## Slide 3: Reducing Miss Penalty
Multi-level Caches
Early Restart/Critical Word First
Sectored Cache

## Slide 4: Multilevel Caches
A memory cannot be large and fast
Add level of cache to reduce miss penalty
  Each level can have longer latency than level above
  So, increase sizes of cache at each level
CPU
L1
L2
DRAM
Metrics:
Local miss rate = misses in cache/ accesses to cache
Global miss rate = misses in cache / CPU memory accesses
Misses per instruction = misses in cache / number of instructions

## Slide 5: Inclusion Policy
Inclusive L2:
  All L1 cache lines are also in L2
  Advantage
    Remote memory access can be serviced by L2
    Remote memory invalidate need not be forwarded to L1 if line not in L2
  Disadvantage
    Reduced overall cache space
    L2 replacement causes L1 invalidation

## Slide 6: Inclusion Policy
Exclusive multi-level caches:
  L1 cache lines are not in L2
  Advantage:
    Increased overall cache space
  Disadvantage:
    Remote memory access and invalidate have to be forwarded to L1

## Slide 7: Inclusion Policy
Non-inclusive multi-level cache
  L1 line may or may not be in L2
    Essentially start as Inclusive (bring line in both L1 and L2)
    L2 replacement does not cause L1 invalidation
  Advantage:
    Remote memory access can be serviced by L2
    More overall cache space than Inclusive
  Disadvantage:
    Remote memory invalidate has to be forwarded to L1, even if line not in L2

## Slide 8: Reducing Miss Penalty
Multi-level Caches
Early Restart/Critical Word First
Sectored Cache

## Slide 9: Early Restart/Critical Word First
Early Restart:
  As soon as the requested word arrives, forward it to CPU
  Miss penalty is now time to fetch the requested word
Critical Word First
  Problem still with Early Restart
    What if requested word is in the middle of the block?
  Start fetching the block with the required (critical) word, and fill in the rest
Almost all L1 caches do both of these

## Slide 10: Reducing Miss Penalty
Multi-level Caches
Early Restart/Critical Word First
Sectored Cache

## Slide 11: Sub-blocking/Sectored Cache
Small Block Size
  Lower Miss Penalty
  Low Spatial Locality
  Larger Tag Array Size
    Suppose 64kB, direct-mapped Cache, 32b addr
      Block Size = 64B  b = 6, k =10, t = (32-10-6) = 16
        Tag Array Size = 2k(1+t) = 17k bits
      Block Size = 32B  b = 5, k = 11, t = (32-11-5) = 16
        Tag Array Size = 2k(1+t) = 34k bits
  Can we get small tag array and low miss penalty?

## Slide 12: Sub-blocking/Sectored Cache
Divide large block into smaller sub-blocks
  Add a valid-bit for each sub-block
  Fetch only sub-block on a miss
  Can prefetch other subblocks in the background
If tag matches, is the word in the cache?
May not be
tag
valid bits
block
sub-block

## Slide 13: Reducing Hit Time
Simpler/Smaller Caches
Delayed Write
Way Prediction
Remove Address Translation from Critical path

## Slide 14: Reducing Hit Time
Simpler/Smaller Caches
Delayed Write
Way Prediction
Remove Address Translation from Critical path

## Slide 15: Direct-Mapped Cache: Read
Tag
Data Block
V
=
Block
Offset
Tag
Index
t
k
b
t
HIT
Data Word or Byte
2k
lines

## Slide 16: Direct-Mapped Cache: Write
Tag
Data
V
=
Block
Offset
Tag
Index
t
k
b
t
HIT
Data Word or Byte
2k
lines
WE
How does write timing compare to read timing?
Completely serial!
Problem: Writes take two cycles in memory stage, one cycle for tag check plus one cycle for data write if hit

## Slide 17: Reducing Write Hit Time with Pipelined/Delayed Write
    Hold write data for store in single buffer ahead of cache
    Write cache data during next idle data access cycle
Time
Data
Tag
LD0
LD0
ST1
ST1
ST2
LD3
LD3
Buffer
ST1
ST2
ST2
ST4
ST2
ST4
LD5
LD5
ST4
LD0 ST1 ST2 LD3 ST4 LD5
On a load, check this buffer.
This buffer is often the LSQ!
Similarly, there is a write buffer before L2

## Slide 18: Reducing Hit Time
Simpler/Smaller Caches
Delayed Write
Way Prediction
Remove Address Translation from Critical path

## Slide 19: Set-Associative Cache: Hit Time
Offset
Tag
Index
Address:
index | v | tag | Data block |  |  | 
2k
lines
k-bits
b-bits
t-bits
v | tag | Data block |  |  | 
Way 0
Way (a-1)
k
=
t
t
=
t
Data
Word
or Byte
b
…
…
a = associativity
Tag check across multiple ways can increase delay

## Slide 20: Way Prediction
Use processor address to index into way prediction table
Look in predicted way at given index, then:
HIT
MISS
Return copy
of data from
cache
Read block of data from next level of cache
MISS
SLOW HIT
(change entry in prediction table)
How effective do you think it is?
Prediction for data is hard.
But what about instructions?
Look in other way(s)

## Slide 21: Reducing Hit Time
Simpler/Smaller Caches
Delayed Write
Way Prediction
Remove Address Translation from Critical path

## Slide 22: Memory “Address”
Student I compiled code:
  ADD R1 R2 R3
  LD R1 0x1000
  …
Student II compiled code:
  ADD R4 R1 R3
  ST R4 0x1000
  …
What is the problem if both students run the code simultaneously?
  Solution Today
    Address from program is a “Virtual” Address
    Dynamically translated to a “Physical” Address before memory access
  0x200
  0xA200
  Address 0x1000 should not be shared.

## Slide 23: Memory “Address”
physical
address
virtual
address
Address
Translation
ISA
Physical Memory
(DRAM)
physical
address
virtual
address
Address
Translation
ISA
Physical Memory
(DRAM)
L2
L1
Problem?
VA to PA translation has to happen before L1 access => increases L1 access time (i.e., hit time).
  Can we design a 1-cycle L1 cache that allows translation to occur in parallel to cache access?
    Stay tuned!

## Slide 24: Memory Management
The Fifties
  Absolute Addresses
  Dynamic Address Translation
The Sixties
  Atlas’ Demand Paging
  Paged Memory Systems and TLBs
Modern Systems
  Virtual Memory

## Slide 25: Absolute Addresses
Early machines only ran one program at a time, with unrestricted access to entire machine RAM and I/O devices
Addresses in a program depended on where the program was to be loaded in memory
But it was more convenient for programmers to write location-independent subroutines/libraries
  How?
Loaders and/or linkers relocate library modules to actual locations in memory when building memory image

## Slide 26: Dynamic Address Translation
Motivation
  In early machines, I/O operations were slow and each I/O transfer involved the CPU
    CPU would initiate I/O and then stall while actual data transfer occurred
    Higher throughput possible if CPU and I/O of 2 or more programs were overlapped.
      What is this called today?
Physical Memory
Prog 1
Prog 2
Multiprogramming!
Notes:     Example: 10K instructions between I/O - 100K instructions during I/O

## Slide 27: Support for Multiprogramming
Location Independent Programs
  Programming and storage management ease
  How can HW help with address translation?
Protection
  independent programs should not affect each other inadvertently
  How can HW help with address protection?
Multiprogramming drove the requirement for resident supervisor software to manage context switches between multiple programs
Physical Memory
Prog 1
Prog 2
OS
Base registers
Bound registers

## Slide 28: Simple Base and Bound Translation
Load X
Program Address Space
Bound
Register
Bounds
Violation?
Main Memory
Current
Segment
Base
Register
+
Physical
Address
Logical
Address
Base and bounds registers are visible/accessible only when processor is running in the supervisor (a.k.a kernel) mode
Base Physical Address
Segment Length
≥

## Slide 29: Separate Areas for Program and Data
Physical Address
Physical Address
Load X
Program Address Space
Physical Memory
Data Segment
Data Bound Register
Data Base Register
+
Bounds Violation?
Program Bound Register
Program Base Register
+
Program Segment
Logical Address
Logical Address
≥
≥
Bounds Violation?
Program Counter
What is the advantage of this separation?
Permits sharing of
program segments.

## Slide 30: Base and Bound Machine
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Data Bound Register
Data Base Register
+
Logical Address
Bounds Violation?
Physical Address
Program Base Register
+
Logical Address
Bounds Violation?
≥
≥
Program Bound Register
Logical Address is precursor to today’s “Virtual” Address
Notes: What will bound violation do?
Throw an “Exception”!

## Slide 31: Memory Fragmentation
72K
Job 1
32K
Job 2
24K
8K
Job 1
32K
Job 2
24K
Job 3
64K
Job 3 starts
Job 1
32K
24K
Job 3
64K
8K
Job 2 finishes
Job 4
32K
Job 4 arrives
Can’t run Job 4, as not enough contiguous space! Must compact.

## Slide 32: Paged Memory Systems
Processor-generated address interpreted as <virtual page number, offset>
A page table contains the physical address of the base of each page
offset
virtual page number
Virtual Address Space for User/Job 1
Page Table
for Job 1
Physical Memory
Pages
0
1
2
3
0
1
2
3
1
0
3
2
Fixed-length pages + indirection through page table  No need for contiguous allocation

## Slide 33: Page Table
Virtual Page Number
Page Offset
Physical Page Number
Page Offset
0xFC51908B
Page Table
Base Register
0
11
12
31
20
Page Table
Virtual Address
0x0015208B
Physical
Address
Physical Address
Main
Memory
Page Table
VirtualAddress

## Slide 34: Private Address Space per User
VA
User 1
Page Table
VA
User 2
Page Table
VA
User 3
Page Table
Each user has a page table
Page table contains an entry for each user page
Physical
Memory
FREE
OS
pages
Notes: OS ensures that the page tables are disjoint.

## Slide 35: Where should the Page Tables reside?
Space required by the page tables is proportional to the address space, number of users, …
  Space requirement is large
  Too expensive to keep in registers
Keep PTs in the main memory
  Needs one reference to retrieve the page base address and another to access the data word
    Doubles the number of memory accesses!

## Slide 36: Page Tables in Physical Memory
VA
User 1
VA
User 2
Page Table for User 1
Page Table for User 2

## Slide 37: A Problem in Early Sixties
There were many applications whose data would not fit in the main memory, e.g., payroll
  Paged memory system reduced fragmentation but still required the whole program to be resident in the main memory
Programmers moved data back and forth from the secondary store by manually overlaying it repeatedly on the primary store
  Tricky programming and Error prone!
Explicitly managing the local store done even today sometimes! e.g., IBM Cell microprocessor in Playstation-3

## Slide 38: Demand Paging in Atlas (1962)
User sees 32 x 6 x 512 words of storage
Secondary
(Drum)
32x6 pages
Primary
32 Pages
512 words/page
Central
Memory
“A page from secondary
storage is brought into the
primary storage whenever
it is (implicitly) demanded
by the processor.”
Tom Kilburn
This was the birth of modern virtual memory systems
Notes: It was arguably one of the world's first supercomputers, and the fastest computer in the world until the release of the CDC 6600.
Early in 1962, when most of the Manchester ATLAS was operational and a few privileged patient users were allowed on the machine, it was said that the computing power in the UK was halved, when it was switched off.
Drum was six times less expensive than magnetic core.

## Slide 39: “Virtual” Memory
A virtual address <VPN, offset> can be mapped either to physical memory (if in use) or to disk
Virtual Address
User 1
DRAM
Disk
“Any problem in CS can be solved by adding one level of indirection”

## Slide 40: “Virtual” Memory
Different processes will have different mappings from virtual to physical addresses, and can freely use the same virtual address
Virtual Address
User 1
DRAM
Disk
Virtual Address
User 2
By allocating distinct regions of DRAM to 1 and 2, they are prevented from reading/writing each others data

## Slide 41: Page Table
Virtual Page Number
Page Offset
Physical Page Number
Page Offset
Page Table
Base Register
0
11
12
31
20
Page Table
Virtual Address
Physical Address
v
PPN
If zero, page not in memory  “Page Fault”

## Slide 42: What just happened?
DRAM became a cache for the Disk!
  Motivation: We want the size of disk (~100-200X larger than Memory) but speed of Memory (~1000x faster than disk)

## Slide 43: Caching vs. Paging
CPU
cache
primary
memory
CPU
primary
memory
secondary
memory
Cache | Page Table
Cache Blocks/Lines (~64B) | Pages (~4K)
Offset  Byte in Block | Offset  Byte on Page
Cache (Index + Tag) | Page Number
Cache Hit ~ 1cycle | Page Hit ~ 100 cycles
Cache Miss ~ 100 cycles (handled by HW) | Page Fault ~ 5M cycles (handled by SW)

## Slide 44: Page Fault
Page access by processor is not in primary memory
  Initiate transfer of page from secondary memory (disk) to primary memory (DRAM)
  If no free page in primary memory, a page is selected to be replaced
  Page table updated

## Slide 45: Paged DRAM Management
Allocation/Insertion
  when a byte/word on the page is requested by the CPU
  Fully associative policy used
    (approximate) LRU replacement
    Writeback dirty data to disk
Lookup
  How to avoid scanning all of memory?
    Use VPN to index into Page Table
    Use <PPN, offset> to index into Memory
    “index” is entire VPN  no “tag”

## Slide 46: Modern Virtual Memory Systems Illusion of a large, private, uniform store
Each program/user assumes it owns a contiguous address space
  Example: 32-bit address  4GB Memory can potentially be available to each user
Protection and Privacy
  Several users, each with their private address space and one or more shared address spaces
Demand Paging
  Ability to run a program larger than the primary memory
  Is there another benefit?
    Portability on machines with different configurations
OS
useri
Primary
Memory
Swapping
Store
VA
PA
mapping
Cost: address translation on each memory reference

## Slide 47: Address Translation (and Protection)
Every instruction and data access needs address translation and protection checks
  A good VM design needs to be fast (~one cycle) and space efficient
Physical Address
Virtual Address
Address
Translation
Virtual Page No. (VPN)
offset
Physical Page No. (PPN)
offset
Protection
Check
Exception?
Kernel/User Mode
Read/Write

## Slide 48: Linear Page Table
Page Table Entry (PTE) contains:
  PPN (physical page number) of the memory-resident page
  Status bits for protection and usage
  A bit to indicate if page exists
OS sets the Page Table Base Register (PTBR) for current user process
Data word
Data Pages
PT Base Register
PPN
PPN
PPN
PPN
PPN
Page Table
VPN
Offset
PPN
PPN
VPN
Offset
Virtual address

## Slide 49: Page Table Example
0x1F060 | 0x00ABCD00
0x1F05C | 0x00E20E00
0x1F058 | 0x000011AA
0x1F054 | 0x00CC00CC
0x1F050 | 0xABBAABBA
0x1F04C | 0x000011AA
0x1F048 | 0x00E30E00
0x1F044 | 0x00E20E00
0x1F040 | 0x00E10000
… | …
0x11018 | 0x00000000
0x11014 | 0x0001EAA0
0x11010 | 0x0001FAA1
0x1100C | 0x00AA0FF0
0x11008 | 0x0001DFF0
0x11004 | 0x0001EFF1
0x11000 | 0x0A001FF1
0x11004
0
1
31
12
11
PPN
v
xxx
usage and protection
PTBR
DRAM
Suppose CPU sends a LD 0x00003050
Page Table Entry (32b = 4 bytes)
Page Size 4KB => Page Offset = 12 bits
Page Offset = 0x050
VPN = 0x00003
PT Index = PTBR+ VPN<<2
= 0x11004 + 0x3 << 2 = 0x11010
PTE = 0x0001FAA1  PPN = 0x0001F, v = 1
PA = 0x0001F050
Data = 0xABBAABBA
What will be the data returned from Memory?
Page Size = 4KB
Notes: Shift by 2 == Multiple by PTE size (i.e., 4)