## Slide 1: Lecture 15: Virtual Memory II
Tushar Krishna
School of Electrical and Computer Engineering
Georgia Institute of Technology
tushar@ece.gatech.edu
ECE4100/ECE6100/CS4290/CS6290
Advanced Computer Architecture
Fall 2016
http://tusharkrishna.ece.gatech.edu/teaching/aca_f16/
Acknowledgment: Lecture slides adapted from MIT EECS 6.823 (Arvind and J. Emer), UCB CS 252 (K. Asanovic) and UW CS 378 (L. Ceze)

## Slide 2: Virtual Memory
Physical Address
Virtual Address
Address
Translation
Virtual Page No. (VPN)
offset
Physical Page No. (PPN)
offset
Protection
Check
Exception?
Kernel/User Mode
Read/Write
Do VPN and PPN need to be the same size?
No
“Any problem in CS can be solved by adding one level of indirection”
Notes: PPNs are often smaller than the VPNs, i.e., virtual memory is large, but physical memory is small.

## Slide 3: Linear Page Table
Page Table Entry (PTE) contains:
  A bit to indicate if page exists
  PPN (physical page number) of the memory-resident page
  Status bits for protection and usage
OS sets the Page Table Base Register (PTBR) for current user process
Data word
Data Pages
PT Base Register
Page Table
VPN
Offset
PPN
VPN
Offset
Virtual address

## Slide 4: Example
0x1F060 | 0x00ABCD00
0x1F05C | 0x00E20E00
0x1F058 | 0x000011AA
0x1F054 | 0x00CC00CC
0x1F050 | 0xABBAABBA
0x1F04C | 0x000011AA
0x1F048 | 0x00E30E00
0x1F044 | 0x00E20E00
0x1F040 | 0x00E10000
… | …
0x11018 | 0x00000000
0x11014 | 0x0001EAA0
0x11010 | 0x0001FAA1
0x1100C | 0x00AA0FF0
0x11008 | 0x0001DFF0
0x11004 | 0x0001EFF1
0x11000 | 0x0A001FF1
0x11004
0
1
31
12
11
PPN
v
xxx
usage and protection
PTBR
DRAM
Suppose CPU sends a LD 0x00003050
Page Table Entry (32b = 4 bytes)
Page Size 4KB => Page Offset = 12 bits
Page Offset = 0x050
VPN = 0x00003
PT Index = PTBR+ VPN<<2
= 0x11004 + 0x3 << 2 = 0x11010
PTE = 0x0001FAA1  PPN = 0x0001F, v = 1
PA = 0x0001F050
Data = 0xABBAABBA
What will be the data returned from Memory?
Page Size = 4KB

## Slide 5: Size of Linear Page Table
Suppose 32b address, 4kB pages, 4B PTE
  Virtual Address space per user?
  Number of pages?
  Size of Page Table per user?
What if we use larger pages, say 1MB?
  + Smaller Page Table
  - Internal Fragmentation (not all memory in a page used)
  - Larger Page Fault penalty (more time to read from disk)
What if 64b addresses?
  Even 1MB pages would require 244 8-byte PTEs (35 TB!)
232 = 4GB
VPN size = 32-12 = 20b => Num pages = 220 = 1M
4B x 220 = 4MB
But not all pages in use at the same time

## Slide 6: Hierarchical Page Table
6
Level 1
Page Table
Level 2
Page Tables
Data Pages
page in memory (DRAM)
p1
offset
p2
Virtual Address from CPU
Page Table
Base Pointer
PTE of a nonexistent page
p1 p2 offset
0
11
12
21
22
31
10-bit
L1 index
10-bit
L2 index
page in disk
“Any problem in CS can be solved by adding one level of indirection”
Or two …

## Slide 7: Page Table Walk (e.g, Sparc V8)
31 11 0
Virtual Address
VPN1 VPN2 VPN3 Offset
31 23 17 11 0
Context
Register
PTBR
PPN
PPN
PPN
Context Table
L1 Table
L2 Table
L3 Table
Physical Address
PPN Offset
Handled by a ”Memory Management Unit (MMU)” in hardware

## Slide 8: Why does hierarchical PT help?
L1 PT Size?
  fits in one page
  is pinned to memory
    cannot be swapped out
    i.e., L1 PT addresses are physical
L2 PT Size?
  Fits in 1M pages
  Some of the L2 PT pages can be swapped out of memory to disk!
    i.e., L2 PT addresses are Virtual Addresses
  When can a PT page be swapped?
    None of the PTEs in the PT point to pages currently in Memory
      Don’t want to cause a page fault during translation when the data is actually in memory
4kB
4MB
Virtual Address from CPU
p1 p2 offset
0
11
12
21
22
31
10-bit
L1 index
10-bit
L2 index
Notes: a page of a PT can be swapped out only
if none its PTE’s point to pages in the
primary memory

## Slide 9: What implications does this have?
We replaced every memory access MEM[addr] with
  MEM[MEM[MEM[PTBR + VPN1<<2] + VPN2<<2] + offset]
  Best Case: 3 Memory References
  Worst Case?
Address translation is too slow!
    How should we deal with this high latency?
“Any problem in CS can be solved by adding a level of indirection”
Except too many levels of indirection!
  2 Page Faults + 3 Memory References

## Slide 10: Introduce a Cache!
Add a new cache for frequently used Virtual to Physical address translations
  Translation Lookaside Buffer (TLB)
  TLB Hit => Single Cycle Translation
  TLB Miss => Page Table Walk to refill
VPN offset
v protection tag PPN
physical address
PPN offset
virtual address
hit?
(VPN = virtual page number)
(PPN = physical page number)

## Slide 11: TLB Designs
Typically 32-128 entries
  usually fully associative. Why?
    Each entry maps a large memory space (4kB), hence less spatial locality across pages  more likely that two entries conflict
  Sometimes larger TLBs (256-512 entries) are 4-8 way set-associative to reduce TLB latency
  Larger systems sometimes have multi-level (L1 and L2) TLBs
  Random or FIFO replacement policy
TLB Reach: Size of largest virtual address space that can be simultaneously mapped by TLB
  Example: 64 TLB entries, 4KB pages, one page per entry
  TLB Reach?
64 entries * 4 KB = 256 KB (if contiguous)

## Slide 12: Is TLB Miss same as a Page Fault?
No
  TLB Miss: Virtual to Physical Translation does not exist in TLB
  Page Fault: The Virtual to Physical Translation does not exist in Page Table
    i.e., the physical page does not exist in memory
    has to be brought in and a translation added into the Page Table Entry
  TLB miss may or may not lead to a page fault

## Slide 13: Handling a TLB Miss
Software (MIPS, Alpha)
  TLB miss causes an exception and the operating system walks the page tables and reloads TLB. A privileged “untranslated” addressing mode used for walk.
  Software TLB miss can be very expensive on out-of-order superscalar processor as requires a flush of pipeline to jump to exception handler.
Hardware (SPARC v8, x86, PowerPC, RISC-V)
  A memory management unit (MMU) walks the page tables and reloads the TLB.
  If a missing (data or PT) page is encountered during the TLB reloading, MMU gives up and signals a Page Fault exception for the original instruction.
Note: TLB is a microarchitectural optimization
  A given ISA can use either TLB miss strategy

## Slide 14: Handling a Page Fault
When the referenced page is not in DRAM:
  A “Page Fault” exception is thrown
    Pipeline flushed
    Control jumps to a kernel instruction
    Page faults are completely handled in software by the OS
      Can take micro-seconds of delay
      Another job may be run on the CPU while the first job waits for the requested page to be read from disk
  The missing page is brought into DRAM from disk (or created if empty)
    If no free pages are left, a page is swapped out
      Pseudo-LRU replacement policy, implemented in software
    Page Table is updated
  Instruction is restarted – this time it will not encounter a page fault

## Slide 15: Handling a Page Fault
Is that all?
  TLB may have stale translations! (as OS updated page table and possibly swapped out some page(s))
    Need to flush the existing translations from TLB
    Known as “TLB Shootdown”
      is an expensive operation

## Slide 16: Putting it all together
Virtual Address
TLB
Lookup
Page Table
Walk
Update TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
(to cache)
miss
hit
denied
permitted
Protection
Fault
hardware
hardware or software
software
SEGFAULT
the page is
Ï Memory Î memory
Restart Instr

## Slide 17: Address Translation in CPU Pipeline
TLBs speed up address translation
  But are still on the critical path before the cache
  At least 2-cycle cache access (TLB + Cache) even if hits in both
How to cope with this additional latency?
PC
Inst TLB
Inst. Cache
D
Decode
E
M
Data TLB
Data Cache
W
+

## Slide 18: Physical or Virtual Address Caches?
CPU
Physical
Cache
TLB
Primary
Memory
VA
PA
PA
Virtual Cache
CPU
VA
PA
TLB
Primary
Memory
VA
Physically Addressed Cache
Physical Index Physical Tag (PIPT)
Virtually Addressed Cache
Virtually Indexed Virtually Tagged (VIVT)

## Slide 19: Virtually Addressed Cache (Virtual Index/Virtual Tag)
PC
Inst. TLB
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Data TLB
Main Memory (DRAM)
Memory Controller
Physical Address
Instruction data
Physical Address
Physical Address
Page-Table Base Register
Virtual Address
Virtual Address
Hardware Page Table Walker
Miss?
Miss?
Translate on miss

## Slide 20: Virtually Addressed Cache
Advantages
  one-step process in case of a hit
Challenges
  Homonym Problem: Same VA can map to two different PAs
    Why?
  Synonym Problem: Different VAs can map to same PA
    Why?
    VAs in different processes
    Shared libraries, shared data etc …

## Slide 21: Handling Homonyms
Flush cache on a context switch
Or
Add ASID (Address Space Identifier) bits to the tags
VA
Tag
Data
ASID

## Slide 22: Synonyms/Aliases in Virtual-Address Caches
VA1
VA2
Page Table
Data Pages
PA
VA1
VA2
1st Copy of Data at PA
2nd Copy of Data at PA
Tag
Data
Two virtual pages share one physical page
Virtual cache can have two copies of same physical data.
Aliases should not coexisting in cache!
Writes to one copy not visible to reads of other!
Why is that a problem?
Notes: Two processes sharing the same file,
Map the same memory segment to different
Parts of their address space.

## Slide 23: Physical or Virtual Address Caches?
CPU
Physical
Cache
TLB
Primary
Memory
VA
PA
PA
Virtual Cache
CPU
VA
PA
TLB
Primary
Memory
VA
Physically Addressed Cache
Physical Index Physical Tag
(PIPT)
Virtually Addressed Cache
Virtually Indexed Virtually Tagged (VIVT)
Physical Cache
CPU
VA
PA
TLB
Primary
Memory
Physically Addressed Cache
Virtually Indexed Physically Tagged (VIPT)

## Slide 24: Physically-Indexed Physically Tagged
VPN
Page Offset (p)
PPN
Page Offset (p)
TLB
VA
PA
Index (k)
tag (t)
Byte offset (b)
=
 | v | tag | Data block |  |  | 
HIT
Page Offset remains the same in VA and PA.
Can we leverage this to access the cache before translation?
..

## Slide 25: Virtually-Indexed Physically Tagged
VPN
Page Offset (p)
PPN
Page Offset (p)
TLB
VA
PA
=
 | v | tag | Data block |  |  | 
HIT
index (k)
tag (t)
Byte offset (b)
index (k)
..
Under what condition will this work?
k+b ≤ p

## Slide 26: VIPT Caches
For 4kB pages and 64B cache lines, what is maximum possible size of direct-mapped cache?
  k = 12-6 = 6 => 26 = 64 lines => 4kB cache
How can we increase the size of VIPT caches?
  k has to be fixed => only way to increase size is to increase associativity
  How scalable is that?
    For 32kB cache, a = 32k/4k = 8
    For 4MB cache, a = 4M/4k = 1024  Not feasible
  Limits size of VIPT caches
Almost all L1s today are VIPT of sizes ~ 16-64kB
Notes: Suppose L = 12 (4KB pages)
For 32KB Cache, W = 32K/4K = 8
For 4MB Cache, W = 4M / 4 K = 1024  Not feasible

## Slide 27: Virtual Memory Today - 1
Desktops/servers have full demand-paged virtual memory
  Portability between machines with different memory sizes
  Protection between multiple users or multiple tasks
  Share small physical memory among active tasks
  Simplifies implementation of some OS features
Vector supercomputers have translation and protection but not demand-paging
  Don’t waste expensive CPU time thrashing to disk (make jobs fit in memory)
  Mostly run in batch mode (run set of jobs that fits in memory)
  Difficult to implement restartable vector instructions

## Slide 28: Virtual Memory Today - 2
Most embedded processors and DSPs provide physical addressing only
  Can’t afford area/speed/power budget for virtual memory support
  Often there is no secondary storage to swap to!
  Programs custom written for particular memory configuration in product
  Difficult to implement restartable instructions
  Given the software demands of modern smartphones, all this may change in the near future!

## Slide 29: Virtual Memory Practice Problem
0x0F038 | 0x0106000B
0x0F034 | 0x0105000B
0x0F030 | 0x0104000B
0x0F02C | 0x00FD000B
0x0F028 | 0x00FC000B
0x0F024 | 0x00FB000B
0x0F020 | 0x00FA000B
0x0F01C | 0x00E4000B
0x0F018 | 0x00E3000B
0x0F014 | 0x00E2000B
0x0F010 | 0x00E1000B
… | …
0x0C00C | 0x0F04000B
0x0C008 | 0x0F03000B
0x0C004 | 0x0F02000B
0x0C000 | 0x0F01000B
0x01000
System PT Base
(Physical)
… | …
0x0100C | ?
0x01008 | ?
0x01004 | ?
0x01000 | ?
0x0C000
User
PT Base
(Virtual)
VPN | PPN
0x0100 | 0x0F01
TLB
System Page Table
(in Physical Space)
User Page Table
(in Virtual Space)
DRAM
20-bit Virtual and Physical Addresses
Page Size = 16B
Linear Page Table with 4B PTE
4 Entry TLB, Fully Associative
Memory Layout:
VA < 0x01000  User
PTE: UPTB+4*(A>>4)
VA > 0x01000  System
PTE: SPTB +4*(A-0x01000)>>4)
PPN
v
xxx
protection
0
1
31
16
15
What is the physical address for VA 0x00030?

## Slide 30: Solution
0x00030 = 32’b00000000000000110000
  VPN = 0x3, Offset = 0
Is there an entry for VPN 0x0003 in the TLB?
    No  TLB Miss
    Let’s go to Page table
    Which page table?
    VA = 0x00030 (< 0x01000)  User Page Table

## Slide 31: Solution
What we know
  VPN = 0x3 (3rd page of this virtual space)
  Page Offset = 0x0
  User Page Table
  User PT Base = 0x01000
  PTE Index = 0x01000 + VPN * Size of PTE
  = 0x01000 + 0x3*4
  = 0x0100C
  Is this a Virtual or a Physical Address?
Virtual

## Slide 32: Solution
Another VA!
  Has to be translated
  0x0100C
    VPN = 0x0100, Offset = 0xC
  Is 0x0100 in the TLB?
    Yes!  TLB Hit
    PPN = 0F01
  VA 0x0100C = PA 0x0F01C
    PA 0x0F01C is the PTE for the original VA 0x00030

## Slide 33: Solution
PTE[0x0F01C] = 0x00E4000B
  PPN = 0x00E4, valid = 1
  This will be cached in the TLB
So VA 0x00030 = PA 0x00E40
VPN | PPN
0x0100 | 0x0F01
0x0003 | 0x00E4