## Slide 1: Lecture 20: Cache Coherence I
Tushar Krishna
School of Electrical and Computer Engineering
Georgia Institute of Technology
tushar@ece.gatech.edu
ECE4100/ECE6100/CS4290/CS6290
Advanced Computer Architecture
Fall 2016
http://tusharkrishna.ece.gatech.edu/teaching/aca_f16/
Acknowledgment: Lecture slides adapted from MIT EECS 6.823 (D. Sanchez) and
GT ECE 4100/6100 CS 4290/6290 (H-S. Lee, T. Conte)

## Slide 2: Shared Memory Programming
Single-Writer Multiple Reader
  Example: a weather simulation program
  Shared variables: Temperature (T) and Pressure (P)
  Reads: All cores read P and T and compute weather conditions across distributed regions (in parallel)
  Write: Cores take turns to periodically update T and P
Multiple-Writer Multiple Reader
  Example: a shared task queue.
  Shared variables: Head (H) and Tail (T) pointers
  Reads: All cores pull tasks from Head
  Writes: All cores push tasks to Tail
Notes: Implemented as parallel threads.

## Slide 3: Shared Memory Multiprocessors
$
$
Processor
Processor
Interconnection Network
$
$
Processor
Processor
…
Main Memory
Today
CMP
NoC

## Slide 4: Example: Case 1
Core 1
Core 2
Core 3
Core 4
Main Memory
Bus
Shared Memory
Core 2: LD T
Core 1: LD T
Core 2: ST T 100
Core 1: LD T
Core 1: ST T 200
T = 250

## Slide 5: Example: Case 2
Core 1
Core 2
Core 3
Core 4
Main Memory
Bus
$
“Shared” Cache
Shared Memory
Core 2: LD T
Core 1: LD T
Core 2: ST T 100
Core 1: LD T
Core 1: ST T 200
T = 250

## Slide 6: Example: Case 3
$
$
Core 1
Core 2
$
$
Core 3
Core 4
Main Memory
Bus
“Private” Cache
Shared Memory
Core 2: LD T
Core 1: LD T
Core 2: ST T 100
Core 1: LD T
Core 1: ST T 200
T = 250
Core 2: LD T
Notes: Core 2’s store won’t propagate to Core 1.
Both write-through and write-back cache will have this problem.
This will not be a problem in a uniprocessor where everything will be serialized.

## Slide 7: Coherence and Consistency
Need to provide illusion of shared memory in the presence of multiple private caches
Intuition: A read should return the most recently written value
  What is “most recent” ?
Formally
  Coherence: What values can a read return?
    Concerns reads/writes to a single memory location
  Consistency: When do writes become visible to reads?
    Concerns reads/writes to multiple memory locations

## Slide 8: Cache Coherence Definition
Preserve Program Order
  If no sharing, each processor acts like a uniprocessor
    A read R from address X on processor P1 returns the value written by the most recent write W to X on P1 if no other processor has written to X between W and R
Write Propagation
  Writes eventually become visible to all processors
    If P1 writes to X and P2 reads X after a sufficient time, and there are no other writes to X in between, P2’s read returns the value written by P1’s write
Write Serialization
  Writes to the same location are serialized: two writes to location X are seen in the same order by all processors.
    Suppose X = 0. P1 increments X to 1, and P2 waits until X is 1 and then increments it to 2. Processor P3 must eventually see that X becomes 1 and then 2 (not the other way round)

## Slide 9: Program Order
LD A
ST A 1
LD A
ST A 2
LD A
Core 0
Core 3
1. LD A
2. ST A 1
3. LD A
4. ST A 2
5. LD A
1. LD A
2. ST A 2
3. LD A
4. ST A 1
5. LD A
ST A 2
LD A
LD A
4. ST A 1
5. LD A
Valid program order
or
or
Note:
Coherence guarantees same order across all cores for same address
Consistency determines order across all cores across different addresses
…
Final A=2
Final A=1
Final A=1

## Slide 10: Why is it hard?
C0
C1
C2
C3
A=1
A=2
T1
T2
A=1
A=1
A=2
A=2
T3
A=1
A=2
A=1
A=2
T4
A=2
A=2
A=1
A=1
What is value of A?
Suppose A=0

## Slide 11: Implementing Coherence
Write Serialization
  Snoopy Protocols
    All caches observe writes in same order on a shared bus
  Directory protocols
    A “directory” tracks content of private caches and serializes requests

## Slide 12: Snoopy Protocols
$
$
Core 1
Core 2
$
$
Core 3
Core 4
Main Memory
Bus
Private Caches
Shared Memory
Snooper
Snooper
Snooper
Snooper
Core and
Snooper
can
change state of cache lines
Core 2: LD T
Core 1: LD T
Core 2: ST T 100
Core 1: LD T
Core 1: ST T 200
T = 250

## Slide 13: Implementing Coherence
Write Propagation
  Update-based protocols
    Update all cached copies after performing the write
  Invalidate-based protocols
    Invalidate all cached copies before performing the write
Typical Policies
  Write-through + Write no-allocate + Update
  Write-back + Write-allocate + Invalidate

## Slide 14: MSI Protocol
State of a block B in a cache $
  Invalid: B is not cached in $
    To read or write, must make a request on the bus
  Modified: B is dirty in $
    C has the block, no other cache has the block, and C must update memory when it displaces B
    Can read or write B without going to the bus
  Shared: B is clean in $
    $ has the block, other caches have the block, and $ need not update memory when it displaces B
    Can read B without going to bus
    To write, must send an upgrade (SM) request to the bus

## Slide 15: MSI Protocol
 | My copy | Others? | Memory | Notes
Modified | Present + Dirty | None | Stale | must write back on replacement
Shared | Present + Clean | Yes (possible) correct, clean | Clean | can discard on replacement
Invalid | Invalid | Unknown | Unknown | 

## Slide 16: CPU Actions  Coherence Actions
Processor
  LD
    Read Hit
    Read Miss + Replacement
  ST
    Write Hit
    Write Miss + Replacement
Bus
  GetS (Get Shared copy)
  GetX (or GetM – Get Exclusive copy)
  PutX (Writeback)

## Slide 17: State Transitions: CPU-initiated
M
S
I
Write Miss / GetX
Read miss / GetS
Replacement
/ PUTX
Write Hit / GetX
Read Hit /--
Write or Read Hit / --
Replacement / --
  CPU Action / Bus Action

## Slide 18: State Transitions: Snooper-initiated
M
S
I
GetX / PUTX
GetS / PUTX
GetS / --
GetX / --
  Observed Bus action / Bus action

## Slide 19: MSI Example
P1
Cache
P2
P3
Bus
Cache
Cache
MEMORY
GETS
Processor Action
State in P1
State in P2
State in P3
Bus Transaction
Data Supplier
S
---
---
GETS
Memory
P1 reads X
X=10
X=10
S

## Slide 20: MSI Example
P1
Cache
P2
P3
Bus
Cache
Cache
MEMORY
X=10
S
Processor Action
State in P1
State in P2
State in P3
Bus Transaction
Data Supplier
S
---
---
GETS
Memory
P1 reads X
P3 reads X
GETS
X=10
S
S
---
S
GETS
Memory
X=10
Response comes from memory – more on this later

## Slide 21: MSI Example
21
P1
Cache
P2
P3
Bus
Cache
Cache
MEMORY
X=10
S
Processor Action
State in P1
State in P2
State in P3
Bus Transaction
Data Supplier
S
---
---
GETS
Memory
P1 reads X
P3 reads X
X=10
S
S
---
S
GETS
Memory
P3 writes X
GETX
---
I
M
I
---
M
GETX
X=10
X=-25
Memory

## Slide 22: MSI Example
P1
Cache
P2
P3
Bus
Cache
Cache
MEMORY
Processor Action
State in P1
State in P2
State in P3
Bus Transaction
Data Supplier
S
---
---
GETS
Memory
P1 reads X
P3 reads X
X=-25
M
S
---
S
GETS
Memory
P3 writes X
---
I
I
---
M
GETX
P1 reads X
GETS
X=-25
S
S
S
---
S
GETS
P3 Cache
X=10
X=-25
Memory

## Slide 23: MSI Example
P1
Cache
P2
P3
Bus
Cache
Cache
MEMORY
Processor Action
State in P1
State in P2
State in P3
Bus Transaction
Data Supplier
S
---
---
GETS
Memory
P1 reads X
P3 reads X
X=-25
M
S
---
S
GETS
Memory
P3 writes X
I
---
M
GETX
P1 reads X
X=-25
S
S
S
---
S
GETS
P3 Cache
X=10
X=-25
P2 reads X
GETS
X=-25
S
S
S
S
GETS
Memory
Memory

## Slide 24: Who responds with data?
Line in M in another cache
  Performs Writeback
  Two implementations
    Snooper puts “Abort” on Bus
      requester has to retry
      Memory will respond with clean data
    Snooper puts “Intervene” on Bus
      Requester should read the writeback data
      Memory should not respond
Line in S in another cache
  Memory responds
    Problem?
Delay
Notes: Delay.
E and O state solves this.