## Slide 1: Lecture 21: Cache Coherence II
Tushar Krishna
School of Electrical and Computer Engineering
Georgia Institute of Technology
tushar@ece.gatech.edu
ECE4100/ECE6100/CS4290/CS6290
Advanced Computer Architecture
Fall 2016
http://tusharkrishna.ece.gatech.edu/teaching/aca_f16/
Acknowledgment: Lecture slides adapted from MIT EECS 6.823 (D. Sanchez) and
GT ECE 4100/6100 CS 4290/6290 (H-S. Lee, T. Conte)

## Slide 2: Mid-semester Feedback Forms
Extra reading material to supplement lectures
  Class Website has reading material from Hennessy and Patterson!
    http://tusharkrishna.ece.gatech.edu/teaching/aca_f16/
Discuss problems in class
  Some examples discussed in class
    Tomasulo’s, ROB, VA  PA, …
  This is not an undergraduate course  less spoon feeding
    Leverage recitations and office hours wisely
    Focus on understanding concepts in class
Pace of lectures
  Just right ~40%, Fast ~60%
  Some topics were expected to be review
    Pipelines and Basic Caches  if you don’t have the background, read appendix from Hennessy and Patterson
  We will go more slowly through Cache Coherence as it is an advanced topic

## Slide 3: Lab 4
Lab 4 is out
  Make sure you start early! I can’t stress this enough
Recitation session on Monday will go through code structure
  Details also in the lab handout
Lab 4 lets you earn up to 5 points (5 absolute points) of extra-credit
  Enough to move a grade

## Slide 4: Back to Cache Coherence
Preserve Program Order
  If no sharing, each processor acts like a uniprocessor
Write Propagation
  Writes eventually become visible to all processors
Write Serialization
  Writes to the same location are serialized: two writes to location X are seen in the same order by all processors.

## Slide 5: Program Order
LD A
ST A 1
LD A
ST A 2
LD A
Core 0
Core 3
1. LD A
2. ST A 1
3. LD A
4. ST A 2
5. LD A
1. LD A
2. ST A 2
3. LD A
4. ST A 1
5. LD A
ST A 2
LD A
LD A
4. ST A 1
5. LD A
Valid program order
or
or
…
Final A=2
Final A=1
Final A=1

## Slide 6: Implementing Coherence
Write Propagation
  Update-based protocols
    Update all cached copies after performing the write
  Invalidate-based protocols
    Invalidate all cached copies before performing the write
    Most common
Typical Policies
  Write-through + Write no-allocate + Update
  Write-back + Write-allocate + Invalidate

## Slide 7: Implementing Coherence
Write Serialization
  Snoopy Protocols
    All caches observe writes in same order on a shared bus
  Directory protocols
    A “directory” tracks content of private caches and serializes requests

## Slide 8: MSI Protocol
 | My copy | Others? | Memory | Notes
Modified | Present + Dirty | None | Stale | must write back on replacement
Shared | Present + Clean | Yes (possible) correct, clean | Clean | can discard on replacement
Invalid | Invalid | Unknown | Unknown | 

## Slide 9: Snoopy Protocols
$
$
Core 1
Core 2
$
$
Core 3
Core 4
Main Memory
Bus
Private Caches
Shared Memory
Snooper
Snooper
Snooper
Snooper
Core and
Snooper
can
change state of cache lines

## Slide 10: State Transitions: CPU-initiated
M
S
I
Write Miss / GetX
Read miss / GetS
Replacement
/ PUTX
Write Hit / Inv
Read Hit /--
Write or Read Hit / --
Replacement / --
  CPU Action / Bus Action
GetX: Get Exclusive
GETS: Get Shared
PUTX: Writeback
Inv: Invalidate

## Slide 11: State Transitions: Snooper-initiated
M
S
I
GetX / PUTX
GetS / PUTX
GetS / --
GetX or Inv / --
  Observed Bus action / Bus action
GetX: Get Exclusive
GETS: Get Shared
PUTX: Writeback
Inv: Invalidate

## Slide 12: State Transitions
M
S
I
Write Miss / GetX
Read miss / GetS
Replacement
/ PUTX
Write Hit / GetX
Read Hit /--
Write or Read Hit / --
Replacement / --
  CPU Action / Bus Action
  Observed Bus action / Bus action
GetS / --
GetS / PUTX
GetX / --
GetX / PUTX

## Slide 13: MSI Example
P1
Cache
P2
P3
Bus
Cache
Cache
MEMORY
GETS
Processor Action
State in P1
State in P2
State in P3
Bus Transaction
Data Supplier
S
---
---
GETS
Memory
P1 reads X
X=10
X=10
S

## Slide 14: MSI Example
P1
Cache
P2
P3
Bus
Cache
Cache
MEMORY
X=10
S
Processor Action
State in P1
State in P2
State in P3
Bus Transaction
Data Supplier
S
---
---
GETS
Memory
P1 reads X
P3 reads X
GETS
X=10
S
S
---
S
GETS
Memory
X=10
Response comes from memory – more on this later

## Slide 15: MSI Example
15
P1
Cache
P2
P3
Bus
Cache
Cache
MEMORY
X=10
S
Processor Action
State in P1
State in P2
State in P3
Bus Transaction
Data Supplier
S
---
---
GETS
Memory
P1 reads X
P3 reads X
X=10
S
S
---
S
GETS
Memory
P3 writes X
INV
---
I
M
I
---
M
INV
X=10
X=-25
Memory

## Slide 16: MSI Example
P1
Cache
P2
P3
Bus
Cache
Cache
MEMORY
Processor Action
State in P1
State in P2
State in P3
Bus Transaction
Data Supplier
S
---
---
GETS
Memory
P1 reads X
P3 reads X
X=-25
M
S
---
S
GETS
Memory
P3 writes X
---
I
I
---
M
INV
P1 reads X
GETS
X=-25
S
S
S
---
S
GETS
P3 Cache
X=10
X=-25
Memory

## Slide 17: MSI Example
P1
Cache
P2
P3
Bus
Cache
Cache
MEMORY
Processor Action
State in P1
State in P2
State in P3
Bus Transaction
Data Supplier
S
---
---
GETS
Memory
P1 reads X
P3 reads X
X=-25
M
S
---
S
GETS
Memory
P3 writes X
I
---
M
INV
P1 reads X
X=-25
S
S
S
---
S
GETS
P3 Cache
X=10
X=-25
P2 reads X
GETS
X=-25
S
S
S
S
GETS
Memory
Memory
Notes: More examples.
Two cores both want to do ST.

## Slide 18: Who responds with data?
Line in M in another cache
  Performs Writeback
  Two implementations
    Snooper puts “Abort” on Bus
      requester has to retry
      Memory will respond with clean data
    Snooper puts “Intervene” on Bus
      Requester should read the writeback data
      Memory should not respond
Line in S in another cache
  Memory responds
    Problem?
Delay
Notes: Delay.
E and O state solves this.

## Slide 19: Shared Memory Programming Examples
Single-Writer Multiple Reader
  Example: a weather simulation program
  Shared variables: Temperature (T) and Pressure (P)
  Reads: All cores read P and T and compute weather conditions across distributed regions (in parallel)
  Write: Cores take turns to periodically update T and P
Shared Memory Implementation
  All cores read T and P in S state
  Updating core converts it to M invalidating copies in other caches
  All cores have to bring it into cache again in S state

## Slide 20: Shared Memory Programming Examples
Multiple-Writer Multiple Reader
  Example: a shared task queue.
  Shared variables: Head (H) and Tail (T) pointers
  Reads: All cores pull tasks from Head
  Writes: All cores push tasks to Tail
Shared Memory Implementation
  Each core reading to queue needs to bring Head in M state, read the value at Mem[Head], and then increment Head by 1
  Each core writing to queue needs to bring Tail in M state, read the value at Mem[Tail], and then increment Tail by 1
  What if some other core also wants to bring Head in M state and invalidates this copy before it is incremented?
    For correctness, need to lock Head and Tail such that no other cache invalidates it while CPU acting on it
    We will talk a little bit about locks when we discuss Memory Consistency
    Most important topic in parallel programming courses

## Slide 21: Optimizations: E State
Read-Modify-Write is very common
  What is the problem with MSI?
Solution: E state (Exclusive, clean)
  If no other sharers, line comes in E instead of S
  Silent upgrades to M without requiring invalidates
  Can respond with data and transition to S
    Memory adds a bit signifying that the Owner for the line is one of the caches (M or E). Useful in on-chip domain since memory latency very high
Send invalidates whenever S to M

## Slide 22: MESI Protocol: CPU Initiated
E
M
S
I
Write Miss / GetX
Read miss / GetS
Replacement
/ PUTX
Write Hit / Inv
Read Hit /--
Write or Read Hit / --
Replacement / --
(if other sharers)
Read miss / GetS
(if no other
sharers)
Read Hit /--
Write Hit /--
  CPU Action / Bus Action

## Slide 23: MESI Protocol: Snooper Initiated
M
S
I
GetX / PUTX
GetS / PUTX
GetS / --
GetX or INV / --
E
GetS / *
GetX / *
* Could respond with data.
Depends on implementation
  Observed Bus action / Bus action
What happens if line in E sees a INV on the bus?
Not possible! No other core should have a copy of the line

## Slide 24: Implementing E
How to detect if there is some other sharer?
  “share” bit (“HITM” on the Intel P6 bus)
    Always 0, except when somebody pulls it to 1
      This is called “hardwired or”
    Suppose P1 sends GETS, and P2 has line in S
      P2 pulls “share” bit to 1
      P1 transitions to S if “share” is 1, to E if “share” is 0

## Slide 25: More Optimizations
Observation: MS requires writeback
  Problem when frequent read-write sharing
  How to defer the writeback?
Solution: O state (Owner, dirty)
  O = S + responsibility of writeback
  On a GETS, MO transition and provide data
    Memory is still stale
  When does data get written back?
    [Or O could be transferred to some other Sharer].
On Eviction.

## Slide 26: Protocols and States
MSI, MESI, MOSI, MOESI
States != Protocols
States are the “destination,” protocol defines “how to get there”
A protocol can support some state=>state transitions but not others
  Example:
    MO or MI on a GETS
  This is the choice of the protocol designer

## Slide 27: False Sharing
What if Core A writes Wordi and Core B writes Wordk ?
  The cache line keeps ping ponging between the cores (i.e., misses and invalidates) because the addresses are in the same block/line
State
Line Addr
Word 0
Word 1
Word N
…

## Slide 28: Split-Transaction and Pipelined Buses
Req
Delay
Response
Req
Delay
Simple, but low throughput
Atomic Transaction Bus
Req1
Delay
Response
Split-Transaction (Non Atomic) Bus
Req2
Req3
Delay
Response
Supports multiple simultaneous transactions
Higher Throughput but Responses out of order
Response

## Slide 29: Non-Atomicity  Transient States
M
S
I
SM
IS
IM
BusReq
BusGnt
BusReq
BusGnt
BusGnt
Stable States
Transient States
Higher Complexity
Race conditions
What if another core sends GETX while one core is in IM?

## Slide 30: Challenges with Snoopy Protocols
Broadcast every request
  Bandwidth and Energy Consumption
Need a network topology with an “ordering” point
  What is the “ordering” point in the Bus?
  Challenge with Bus?
  Other possible topologies?
  Will a Mesh work?
Bus Arbiter
Tree
Bandwidth
Not as-is
[See Agarwal et al., In-Network Snoop Ordering, HPCA 2009]