## Slide 1: Lecture 22: Cache Coherence III
Tushar Krishna
School of Electrical and Computer Engineering
Georgia Institute of Technology
tushar@ece.gatech.edu
ECE4100/ECE6100/CS4290/CS6290
Advanced Computer Architecture
Fall 2016
http://tusharkrishna.ece.gatech.edu/teaching/aca_f16/
Acknowledgment: Some Lecture slides adapted from MIT EECS 6.823 (D. Sanchez)

## Slide 2: States and Protocols
States: MSI, MESI, MOSI, MOESI
  Transient states: IM, IS, SM, etc …
Protocols: state transition rules + NoC messages
  Triggered by request from CPU or NoC
  Protocol designer defines the rules
    Example:
    State (S):
      if (Write Miss) then next_state = (SM)
      out_message = GETX
    State (IM):
      if (recv == data) then next_state = M
      if (recv == GETX) then next_state = State (IMI)
  Snoopy and Directory

## Slide 3: False Sharing
What if Core A writes Wordi and Core B writes Wordk ?
  The cache line keeps ping ponging between the cores (i.e., misses and invalidates) because the addresses are in the same block/line
State
Line Addr
Word 0
Word 1
Word N
…

## Slide 4: Split-Transaction and Pipelined Buses
Req
Delay
Response
Req
Delay
Simple, but low throughput
Atomic Transaction Bus
Req1
Delay
Response
Split-Transaction (Non Atomic) Bus
Req2
Req3
Delay
Response
Supports multiple simultaneous transactions
Higher Throughput but Responses out of order
Response

## Slide 5: Non-Atomicity  Transient States
M
S
I
SM
IS
IM
BusReq
BusGnt
BusReq
BusGnt
BusGnt
Stable States
Transient States
Higher Complexity
Race conditions
What if another core sends GETX while one core is in IM?
Notes: What if another core sends GETX while one core is in IM?
More transient states!

## Slide 6: Challenges with Snoopy Protocols
Broadcast every request
  Bandwidth and Energy Consumption
Need a network topology with an “ordering” point
  What is the “ordering” point in the Bus?
  Challenge with Bus?
  Other possible topologies?
  Will a Mesh work?
Bus Arbiter
Tree
Bandwidth
Not as-is
[See Agarwal et al., In-Network Snoop Ordering, HPCA 2009]

## Slide 7: Directory Protocols (Censier and Feutrier, 1978)
Snoopy Protocol
  Broadcast Request over memory bus
  Difficult to scale
  Requires additional bandwidth and tag lookups
$
$
P1
P2
$
$
P3
P4
Mem
$
$
P1
P2
$
$
P3
P4
Mem
Bus
Interconnection Network
Directory
Directory Protocol
  Send messages only to cache lines that might have line
  Can scale to more processors
  Requires extra directory storage to track sharers