## Slide 1: Lecture 24: Cache Coherence V
Tushar Krishna
School of Electrical and Computer Engineering
Georgia Institute of Technology
tushar@ece.gatech.edu
ECE4100/ECE6100/CS4290/CS6290
Advanced Computer Architecture
Fall 2016
http://tusharkrishna.ece.gatech.edu/teaching/aca_f16/
Acknowledgment: Some Lecture slides adapted from MIT EECS 6.823 (D. Sanchez)

## Slide 2: MSI Directory
Core 0
Main Memory
Cache 0
Tag | State | Data
Directory
Tag | State | Sharers
Core 1
Cache 1
Tag | State | Data
Core 2
Cache 2
Tag | State | Data
    Uncached (Un) : No sharers
    Shared (Sh) : one or more sharers with Read permssion (S)
    Exclusive (Ex) : single sharer with R & W permission (M)
  list of cores sharing the line. Implemented as a bit-vector, one per core
    M / S / I
For simplicity, let us consider MSI protocol

## Slide 3: Cache Transitions and Messages
M
S
I
PrWr / --
PrRd / --
PrRd / --
PrWr / ExReq
PrRd / ShReq
PrWr
/ ExReq
M
S
I
Eviction/
WbReq
(With data)
Eviction
/ EvReq
(without data)
why?
Directory keeps updated sharers list
M
S
I
DownReq /
DownResp
(with data)
InvReq /
InvResp
(without
data)
InvReq /
InvResp
(with
data)
In Request / Out Message
Transition states not shown
Processor Initiated
Eviction Initiated
Directory Initiated
another core sent ShReq
 another core sent ExReq

## Slide 4: Directory Transitions and Messages
Un
Sh
Ex
Un
Sh
Ex
ExReq (P)/
ExResp(P) /
Sharers = {P}
ExReq (P) /
InvReq(sharers)
+ ExResp (P) /
Sharers = {P}
ShReq (P)/
ShResp(P) /
Sharers = {P}
ShReq (P)/
ShResp(P) /
Sharers = Sharers + {P}
ShReq (P) /
DownReq(sharer)
+ ShResp (P) /
Sharers
= Sharers + {P}
EvReq (P)
&& |Sharers| > 1
EvResp(P) /
Sharers = Sharers - {P}
EvReq (P)
&& |Sharers| == 1
EvResp(P) /
Sharers = { }
WbReq (P) /WbResp(P) /
Sharers = { }
In Request /
Out Message /
Sharer List
Data Req Initiated
Wb/Ev Req Initiated

## Slide 5: Transient States
M
S
I
SM
IS
IM
Req
Resp
Req
Resp
Resp
Req
Req
(Pr or Eviction or Dir)
?
“Race Conditions”
Adds a lot of complexity to protocols

## Slide 6: Example
Core 0
Main Memory
Cache 0
Tag | State | Data
Directory
Tag | State | Sharers
Core 1
Cache 1
Tag | State | Data
Core 2
Cache 2
Tag | State | Data
Tag | State | Data
0xA | IS | 
Tag | State | Data
0xA | S | 3
2
ShReq 0xA
Tag | State | Sharers
0xA | Sh | {0}
Mem[0xA] = 3
4
ShResp 0xA, data=3
3
LD 0xA
1

## Slide 7: Example
Core 0
Main Memory
Cache 0
Tag | State | Data
0xA | S | 3
Directory
Tag | State | Sharers
0xA | Sh | {0}
Core 1
Cache 1
Tag | State | Data
Core 2
Cache 2
Tag | State | Data
LD 0xA
1
Tag | State | Data
0xA | IS | 
Tag | State | Data
0xA | S | 3
2
ShReq 0xA
Tag | State | Sharers
0xA | Sh | {0,2}
Mem[0xA] = 3
4
ShResp 0xA, data=3
3

## Slide 8: Example
Core 0
Main Memory
Cache 0
Tag | State | Data
0xA | S | 3
Directory
Tag | State | Sharers
0xA | Sh | {0,2}
Core 1
Cache 1
Tag | State | Data
Core 2
Cache 2
Tag | State | Data
0xA | S | 3
ST 0xA
1
Tag | State | Data
0xA | IM | 
Tag | State | Data
0xA | I | 3
2
ExReq 0xA
Tag | State | Sharers
0xA | Ex | {1}
Mem[0xA] = 3
5
3
InvReq 0xA
3
InvReq 0xA
4
InvResp 0xA
4
InvResp 0xA
6
ExResp 0xA
data = 3
Tag | State | Data
0xA | I | 3
Tag | State | Data
0xA | M | 5
Notes: Silent Eviction at Core 0
Race Condition: Cache 0 receives InvReq but line is in I state.
It should send InvResp.

## Slide 9: Example
Core 0
Main Memory
Cache 0
Tag | State | Data
0xA | I | 3
Directory
Tag | State | Sharers
0xA | Ex | {1}
Core 1
Cache 1
Tag | State | Data
0xA | M | 5
Core 2
Cache 2
Tag | State | Data
ST 0xB
1
Tag | State | Data
0xA | I | 3
4
WbResp 0xA
Tag | State | Sharers
0xA | Un | {}
2
WbReq 0xA, data=5
Mem[0xA] = 5
3
5
ExReq 0xB
Mem[0xB] = 10
6
Tag | State | Sharers
0xB | Ex | {1}
7
ExResp 0xB, data=10
Why are 0xA’s wb and 0xB’s req serialized?
Structural dependence
Tag | State | Data
0xA | MI | 5
Writeback 0xA!
Tag | State | Data
0xB | IM | 
Tag | State | Data
0xB | M | 10

## Slide 10: Miss Status Handling Register
Buffer to hold coherence requests and writebacks outside cache
On Cache Miss or Writeback
  Allocate entry in MSHR
  If MSHR full  Stall
On Data response from Memory
  Forward data to CPU and cache
  Deallocate MSHR

## Slide 11: Example
Addr | State | Data
Core 0
Main Memory
Cache 0
Tag | State | Data
0xA | I | 3
Tag | State | Sharers
0xA | Ex | {1}
Core 1
Tag | State | Data
0xA | M | 5
Core 2
Cache 2
ST 0xB
1
Tag | State | Data
0xB | IM | 
4
WbResp 0xA
Tag | State | Sharers
0xA | Un | {}
2
WbReq 0xA, data=5
Mem[0xA] = 5
3
2
ExReq 0xB
Mem[0xB] = 10
3
0xB | Ex | {1}
Tag | State | Data
0xB | M | 10
4
ExResp 0xB, data=10
Addr | State | Data
0xA | M->I | 5
Addr | State | Data
0xA | I | 
MSHR
Cache 1
Directory

## Slide 12: Challenges
Correctness
  Protocol Races
  Protocol-level Deadlock
Optimizations
  Inclusion for multi-level caches
  3-hop protocols
  Scalability of Directories

## Slide 13: Protocol Races
Core 0
Main Memory
Cache 0
Tag | State | Data
0xA | S | 3
Directory
Tag | State | Sharers
0xA | Sh | {0,2}
Core 1
Cache 1
Tag | State | Data
0xA | S | 3
ST 0xA
1’
2
ExReq 0xA
3
InvReq 0xA
Tag | State | Data
0xA | SM | 3
ST 0xA
1
2’
ExReq 0xA
ReqQ
1, ExReq 0xA
Tag | State | Data
0xA | SM | 3
Caches 0 and 1 issue simultaneous ExReqs
Directory starts serving cache 0’s ExReq, queues cache 1’s
Cache 1 expected ExResp, but got InvReq!
Cache 1 should transition from SM to IM and send InvResp
What should Cache 1 do?

## Slide 14: Protocol-level deadlock
Protocols can deadlock even though network is deadlock-free
  Eg: Both nodes saturate all intermediate buffers with requests to each other, blocking responses from entering the network
  Solution: Separate Virtual Networks for each class of message
    Implemented as Virtual Channels over same physical links
    Most protocols need at least 2 virtual networks
Cache 0
Directory
req
req
req
req
req
req
req
req
resp
resp

## Slide 15: Challenges
Correctness
  Protocol Races
  Protocol-level Deadlock
Optimizations
  Inclusion for multi-level caches
  3-hop protocols
  Scalability of Directories

## Slide 16: Multi-level caches
L1
L1
P1
P2
$
$
P3
P4
Mem
L2
L2
Directory
$
$
Pi
j
L2
Interconnection Network
1
2
3
4
5
6
  With Inclusive L2, 3 and 4 can be avoided.
Suppose P3 sends a Exclusive Request
2
5
3
4
  (holds for both Snoopy
  and Directory protocols)
  Faster Response
  Snooping in L2 does not affect CPU-L1 bandwidth
Notes: If both CPU-L1 and L2-Bus interactions involve the same address, stalls will be required.

## Slide 17: 3-Hop Protocols
How many hops typically to get data in M?
  Optimization: Cache-to-Cache Transfer
Core 0
Main Memory
Cache 0
Tag | State | Data
0xA | M | 3
Directory
Tag | State | Sharers
0xA | Ex | {0}
Core 1
Cache 1
Tag | State | Data
Core 2
Cache 2
Tag | State | Data
ST 0xA
1
Tag | State | Data
0xA | IM | 
Tag | State | Data
0xA | I | 3
2
ExReq 0xA
Tag | State | Sharers
0xA | Ex->Ex | {2}
3
ExFwd 0xA, req=2
Tag | State | Data
0xA | M | 3
3
ExResp 0xA, data=3
ExAck 0xA
4
Tag | State | Sharers
0xA | Ex | {2}
4

## Slide 18: Directory Implementation
How many directory entries are needed in total?
  Number of unique cache lines on-chip
Where should directory be stored?
  If Private Caches at Level N, Directory should be at Shared Level N+1
  Typically stored as state in the Last Level Cache (LLC) on-chip which is L3 nowadays
    If no LLC on-chip, stored in Memory with a Directory Cache on-chip for fast lookups
      Example – a lot of designs just have Private L1 and Private L2

## Slide 19: On-Chip Cache Organizations: Private L2
L1 Miss?
  Lookup local L2
L2 Hit?
  Done
L2 Miss?
  Go to Directory
Directory Hit?
  Perform Coherence transactions
  Bring data from Memory
Directory Miss
  Bring data and directory entry from memory
P
Private
L1
Private
L2 slice
Router
Memory Controller
Directory

## Slide 20: On-Chip Cache Organizations: Shared L2
P
Private
L1
Router
Uniform Cache Access
Memory Controller
Directory
Shared L2 / LLC
L1 Miss?
  Lookup shared L2
L2 Hit?
  Perform coherence transactions
  Send data from L2
L2 Miss
  Bring data and directory entry from memory

## Slide 21: Example: Intel Haswell (2013)
22nm
Private L1 Per Core
  L1D = 32kB
  L1I = 32kB
Private L2 Per Core
  L2 = 256kB
Shared L3
  8-20 MB

## Slide 22: Directory Scalability
Distributed Directories
Limited Directories

## Slide 23: Directory Scalability: Bandwidth into Directory
P0
$
P13
$
P14
$
P15
$
Memory
Interconnection Network
P1
$
Directory
Classic Problem with Large Central Table
High Access time
High Access Energy
Low Bandwidth
P
$
Memory
Interconnection Network
P
$
Memory
P
$
Memory
P
$
Memory
P
$
Memory
P
$
Memory
Directory
Directory
Directory
Directory
Directory
Directory
Distributed Directories
Called “CC-NUMA”
  Cache Coherent NUMA
Each address has a “Home Node” – the directory the request goes to

## Slide 24: On-Chip Cache Organization: Shared Distributed L2 [NUCA]
P
Private
L1
Directory
slice
Shared
L2 slice
Router
offset
index
tag
Home node ID
Most common Implementation:
static partitioning of address space
Distribute shared L2 (LLC) and directory across tiles
“Banked L2”
Address
Non Uniform Cache Access
Memory Controller

## Slide 25: On-Chip Cache Organization: Shared Distributed L2 [NUCA]
L1 Miss?
  Send coherence request to shared L2 (LLC)
  Which L2 (LLC) slice?
    At Home Node
L2 Hit ?
  Perform coherence actions based on Directory state
L2 (LLC) Miss?
  Go to Memory
P
Private
L1
Directory
slice
Shared
L2 slice
Router
Memory Controller
Non Uniform Cache Access

## Slide 26: Private vs Shared L2 Designs
Suppose we have the same amount of L2 storage
  Should we design it as Private L2s or Shared L2?
    Hint: No “Correct” Answer
Private L2
  Pros?
  Cons?
Shared L2
  Pros?
  Cons?
  Higher access latency (higher L1 Miss Penalty) since every L1 miss uses NoC
More overall capacity
Fast Access
Replication of lines  lower overall capacity

## Slide 27: Can we get the best of both?
Approach 1: Intelligent Data Placement
  Private Caches with low replication
  Shared Caches with Home Node close to / at the core accessing it
    Leverage OS for optimal “page coloring” or a dynamic home node
Approach 2: Fast Network
  Networks with fast access to home nodes via fast links (e.g., optical) topology or flow-control mechanisms
Website has extra readings on these

## Slide 28: Directory Scalability
Distributed Directories
Limited Directories

## Slide 29: Managing Directory Overhead
For a N-core system, how many bit of storage per directory entry?
  Tag?
    Part of tag storage of LLC so need not be counted as Directory overhead
  State?
  Sharer List?
Is that scalable?
  2-bit [Sh, Ex, Un] + intermediate states
N-bit

## Slide 30: Limited Directories
Do not track all sharers
  For instance, directory only tracks up to 4 sharers, and beyond that broadcasts
  Often programs do not exhibit heavy sharing so this is an acceptable trade-off for optimizing for the common case
  Example: early AMD Opterons (~2005): Just track the Owner, no sharers

## Slide 31: Next …
Coherence: What values can a read return?
  Concerns reads/writes to a single memory location
Consistency: When do writes become visible to reads?
  Concerns reads/writes to multiple memory locations